## Slide 1
Watershed Management & Water Quality

## Slide 2
Water quality is one of the main challenges that societies will face during the 21st century, threatening human health, limiting food production, reducing ecosystem functions and hindering economic growth.
Water quality degradation translates directly into environmental, social and economic problems.
The availability of the world’s scarce water resources is increasingly limited due to the worsening pollution of freshwater resources caused by the disposal of large quantities of insufficiently treated, or untreated, wastewater into rivers, lakes, aquifers and coastal waters.

## Slide 3
Furthermore, newly emerging pollutants like personal care products and pharmaceuticals, pesticides, industrial and household chemicals, and changing climate patterns represent a new water quality challenge, with still unknown long-term impacts on human health and ecosystems.
Water pollution, resulting from human activities, disturbs aquatic ecosystems not only in structure but also in function, affecting and modifying the integrity of these systems.
Clear evidence is eutrophication, which results from high loads of nutrients (phosphorus and nitrogen) primarily from agricultural runoffs, domestic and industrial wastewater and atmospheric inputs from fossil fuel burning.

## Slide 4
Acidification is another concerning threat putting more pressure on the complex dynamics of lakes, wetlands and reservoirs.
In addition to its health and socio-economic impact, water quality degradation relates directly to biodiversity loss, reduced ecosystem functioning and the unsuitability of water for various uses due to pollution of water resources.
Water pollution thus constitutes a serious threat not only to securing enough water of good quality for human needs, but also to meeting the ecosystem needs and maintaining environmental flows.

## Slide 5
Water quality involves a long list of individual components and physical, chemical, and biological constituents.
A water-quality standard refers to the physical, chemical, or biological characteristics of water in relation to a specified use
For example, water-quality standards for irrigation are not necessarily acceptable for drinking water.
Changes in water quality resulting from land-use activities on a watershed can make water unusable for drinking but it can still be acceptable for irrigation or other uses.

## Slide 6
Hence, Watershed management is Important for:
  Assessment of water quantity
  Assessment & monitoring of water quality – livelihoods of watershed dwellers
Water Quality – examination to determine organisms, minerals & organic compounds in water
  Depending on use of water
  Physico-chemical, chemical & microbiological analyses of water
Common issues of Surface and Groundwater quality are:
  Pathogenic (Bacteriological) Pollution; Salinity
  Toxicity (micro-pollutants and other industrial pollutants)

## Slide 7
Water Quality Standards
  It is a measure of the condition of water relative to the requirements of one or more biotic species and/or to any human need or purpose.
  It is most frequently used by reference to a set of standards against which compliance can be assessed.
  The most common standards used to assess water quality relate to
    health of ecosystems,
    safety of human contact and drinking water.

## Slide 8
Water Quality Categories
  Human consumption
    Drinking water, including bottled water, may reasonably be expected to contain at least small amounts of some contaminants.
    Presence of these contaminants does not necessarily indicate that water poses a health risk.
  Industrial use
    Dissolved minerals may affect suitability of water for a range of industrial purposes.
    presence of ions of Ca and Mg which interfere with the cleaning action of soap, & can form hard sulfate and soft carbonate deposits in water heaters/boilers.
    Hence’ hard water may be softened to remove these ions.
    Softening may sacrifice nutrition for cleaning effectiveness.

## Slide 9
In the environment.
  Toxic substances and high populations of certain microorganisms can present a health hazard for non-drinking purposes such as irrigation, swimming, fishing, boating, and industrial uses.
  These conditions may also affect wildlife, which use the water for drinking or as a habitat.
Irrigation purpose,
  Crop production – irrigation water quality requirements
    Agriculture- single largest user of freshwater - a major cause of degradation of surface and groundwater resources through erosion and chemical runoff

## Slide 10
Water Pollution Sources
  Water pollution is the contamination of water bodies e.g. lakes, rivers, oceans and groundwater.
  Water pollution occurs when pollutants are discharged directly or indirectly into water bodies without adequate treatment to remove harmful compounds.
  Water pollution affects plants and organisms living in these bodies of water.
  The effect is damaging to individual species and populations and natural biological communities.

## Slide 11
Water Pollution Source Types
  Point sources or
  Non-point sources
Point sources:
  Contaminants that enter a waterway from a single, identifiable source, such as a pipe or ditch.
  Traced to a specific source
  Leaking effluents coming from a waste treatment or industrial plant
Examples
  Discharges from a sewage treatment plant; A factory; A city storm drain;
  Municipal storm sewer systems;
  Industrial storm water, such as from construction sites

## Slide 12
Non–point source pollution (NPS):
  Contamination that does not originate from a single discrete source.
  NPS pollution is the cumulative effect of small amounts of contaminants gathered from a large area.
  Pollutants will come from wide spread area
  They can’t be traced to a single point or source
Examples: Soil erosion, chemical runoff, animal waste pollution
  leaching out of fertilizers/nutrients from agricultural lands.
  Nutrient runoff in storm water- agricultural field/forest.
  Contaminated storm water washed off of parking lots, roads and highways called urban runoff highways, runoff,

## Slide 14
Specific Sources
  Septic systems: Use a large tank buried in the ground to contain and break down household sewage; Fats, oils, and grease as well as large waste particles, are stored and later pumped out of the holding tank; source of concern for groundwater pollution & surface water pollution
  Waste Disposal: Underground or above ground disposal practices of domestic, municipal, or industrial liquid waste
  Industrial liquid waste: treated/ untreated
  Solid waste: Land disposal of municipal and industrial solid waste – leaching
  Mining operations: Mines, Oil & gas- Acid mine drainage, Leaching of toxic metals, Wastewater generated

## Slide 15
Causes of Water Pollution
  Wide spectrum of chemicals, pathogens, and physical or sensory changes such as elevated temperature and discoloration.
  Natural occurring – eg. Salts, fluoride, arsenic, Ca, Mg, Na etc.
  Artificial – disposed by humans from various sources
  Water's physical chemistry includes acidity (change in pH), electrical conductivity, temperature, and eutrophication

## Slide 16
Water Pollution Types
  Organic pollutants
    Detergents; Disinfection by-products
    Food processing waste, fats and grease
    Insecticides & herbicides, and other chemical compounds
    Petroleum hydrocarbons, including fuels (gasoline, diesel fuel, jet fuels, and fuel oil) & lubricants (motor oil), & fuel combustion byproducts
    Tree and bush debris from logging operations
    Volatile organic compounds (VOCs), such as industrial solvents.
    Chlorinated solvents, dense non-aqueous phase liquids (DNAPLs),
    Various chemical compounds found in personal hygiene & cosmetic products

## Slide 17
Inorganic pollutants
  Acidity caused by industrial discharges (sulfur dioxide from power plants)
  Ammonia from food processing waste
  Chemical waste as industrial by-products
  Fertilizers containing nutrients- nitrates and phosphates- which are found in storm water runoff from agriculture, as well as commercial and residential use
  Heavy metals from motor vehicles (via urban storm water runoff) and acid mine drainage
  Silt (sediment) in runoff from construction sites, logging, slash and burn practices or land clearing sites

## Slide 18
Macroscopic - Large visible items polluting the water— may be termed "floatables" in an urban storm water context, or marine debris when found on the open water
  Trash or garbage (e.g. paper, plastic) discarded by people on the ground
  Dumping of rubbish, that eventually discharged into surface waters
Microscopic pollutants – micro organisms, dissolved/ dispersed pollutants
Thermal pollution: The rise or fall in the temperature of a natural body of water caused by human influence.
  It results in a change in the physical properties of water.
  A common cause of thermal pollution is the use of water as a coolant by power plants and industrial manufacturers.

## Slide 19
  Elevated water temperatures decreases oxygen levels (which can kill fish) and affects ecosystem
  Urban runoff may elevate temperature in surface waters.
  Thermal pollution can also be caused by the release of very cold water from the base of reservoirs into warmer rivers.

## Slide 20
Important Water Quality Parameters
  Important physicochemical parameters to be tested for ascertaining water quality are:
    pH; Color, Taste and Odour, Turbidity, TDS, total hardness, chlorides, sulphates, fluorides, nitrates, calcium, heavy metals, dissolved oxygen, pesticides, detergents & radio-nuclides
    pH neutral (Ph = 7); acidic (pH<7); basic (pH>7); drinking water (6.5-8)
    Electrical conductivity – water ability to conduct electrical current depends on concentration of dissolved, associated substances

## Slide 21
Odour, Colour & Taste:
  Odour – classified as: very weak, weak, clear, strong or very strong
  Colour – tested using colorimter tubes – expressed in Hazen standard unit
  Taste – purest form tasteless
Turbidity – caused by presence of suspended matter – ranges in size from colloidal to coarse dispersions – measured by Nephelo/turbidity meter & expressed in NTU (Nephelometric turbidity unit) – indicator necessity of treatment

## Slide 22
Dissolved oxygen – indicates amount of oxygen gas dissolved in water – solubility of atmospheric oxygen in fresh water ranges from 14.6 mg/l at 0oC to about 7 mg/l at 35oC under 1 atmospheric pressure measured using DO meter.
The Biochemical Oxygen Demand (BOD) is an index of the oxygen-demanding properties of biodegradable material in water.
BOD – amount of dissolved O2 demanded by bacteria during stabilization of the decomposable organic matter under aerobic conditions

## Slide 23
Nitrate- water soluble molecule made up of nitrogen & oxygen – natural constituent of plants
  In natural form water contains less than 1mg/liter of nitrate nitrogen but higher levels can cause contamination
  common sources: fertilizers, animal wastes etc. – max. permissible 10ppm

## Slide 24
Chlorides – from dissolved salt deposits, discharge of effluents etc
  maximum limite: 250 ppm
Fluorides - fluorine containing compounds - fluorides - found naturally in low concentration in drinking water and foods
  Fresh water between 0.01–0.3 ppm,
  ocean contains between 1.2-1.5 ppm;
  Maximum permissible 1ppm. = more fluorine – diseases like skeletal fluorosis

## Slide 25
Hardness – represents total concentration of Ca & Mg ions – ppm (weight/ volume)
  Hard water is generally not harmful to one's health, but can pose serious problems in industrial settings.
Iron - naturally occurring and not hazardous
  recommended limit – 0.3mg/liter.
Heavy Metals: Arsenic, Cadmium, Chromium, Copper, Iron, Manganese, Mercury, Nickel, Silver, Zinc etc. are present in as minerals in soils;
  also artificially from man made things – some of these – major contaminations
  determined by AAS (atomic absorption sepctro-photometer), polarography or colorimetry.
  Arsenic – WHO guideline < 0.05 mg/l

## Slide 26
Pesticides: - harmful health effects such as cancer; eg. DDT,
Detergents, phenol, radio-nuclides etc. - WHO guideline <0.5 mg/l
Microbes – indicator potential water borne diseases–bacteria viruses & pathogenic protozoa;
  eg. Coliform bacteria.

## Slide 27
Observed Problems | Causes
Water turns black, smell | Waste water
Acidic taste | Low pH
Alkaline taste | High pH
Boiled Rice hard and yellow | High Alkalinity
White deposits on boiling | Hardness
Iron taste, change in color after exposure to atmosphere, change in Presence of color of cloths, utensils Oily appearance on top of water body | Presence of Iron compounds
Soap not lathering | hardness
Brownish black streaks on teeth | Fluoride
Growth of Algae | Nitrate, phosphate
Fish kills | Low pH, less DO
Salty taste | chloride

## Slide 28
Water quality for environmental indicators in relation to watersheds
  Physical assessment: Total suspended solids (TSS); Temperature; Turbidity; Total dissolved solids (TDS)
  Chemical assessment: PH; Dissolved oxygen (DO); Biochemical oxygen demand (BOD); Total dissolved solids (TDS); Nutrient concentration/toxins;
  Biological assessment: pathogens; Exotic species

## Slide 29
Physical components
  Total suspended solids (TSS) =
    a measure of the concentration of suspended sediments in water.
    It indicates the degree of erosion that is taking place or has taken place in the watershed.
    Measured through water sampling and filtration technique.
  b. Temperature = the hotness or coldness of water in the stream.
      It can affect biological organisms directly and indirectly.
      Temperature affects the amount of dissolved oxygen in water.
      Measured using portable multi-parameter instruments.

## Slide 30
  c. Turbidity
    refers to the clarity of water.
    It impacts the amount of sunlight a stream receives.
    Similarly, it determines the depth the sunlight reaches.
    Turbidity is measured using a Secchi disk or a turbidity meter.
2. Chemical components
  pH
    A measure of the alkalinity or acidity of water.
    Highly impacts aquatic organisms and solubility of nutrients in water.
    Measured using a pH meter.

## Slide 31
b. Dissolved oxygen (DO)
  amount of oxygen present in water.
  It affects aquatic organisms from micro to macro level.
  Measured using a DO meter.
c. Biological oxygen demand (BOD)
  a measure of the amount of oxygen bacteria will consume while decomposing organic matter under aerobic conditions.
  It affects the amount of DO in water.
  Measured by taking samples in the field and analyzed in the laboratory.

## Slide 32
d. Dissolved solids
  refers to the amount of dissolved nutrients in water, as total dissolved solids (TDS).
  Measured using a conductivity meter.
e. Nutrient concentration/toxins
  refers to the presence or absence of a chemical contaminant, one that exceeds the safe level.
  It is of great significance in determining the usefulness of water and the health of the aquatic ecosystem.
  Measured by taking samples in the field and analyzed in the laboratory.

## Slide 33
3. Biological components
  a. Pathogens
    refers to the biological contaminant that poses serious health concern.
    Measured by analyzing fecal coliform count, specifically Escherichia coli species, from the water sample.
  b. Exotic species
    refers to non-native aquatic organisms that were introduced in the river/lake system.
    Normally of concern since it creates havoc to the overall health of the aquatic ecosystem.

## Slide 34
READING ASSIGNMENT
  Read, understand and take important notes on water quality characteristics in relation to watershed management from:
    CHAPTER -11 of Brooks N.K. et al, 2013, HYDROLOGY AND THE MANAGEMENT OF WATERSHED

## Slide 35
Nonpoint source pollution and water-quality characteristics in a watershed
  Nonpoint-source pollution (NPS) refers to pollution that is associated with land-use activities such as agricultural cultivation, grazing of livestock, and forest management practices which can occur in an unnoticeable manner over wide areas
Chemistry of precipitation
  Air pollution and its influence on precipitation chemistry and dry-deposition additions to terrestrial and aquatic systems are of interest to watershed managers, farmers, and society as a whole.

## Slide 36
Acid Precipitation and Atmospheric Chemical Constituents
  Acid refers to pH values less than 7 in water where pH is defined as the negative log (base 10) of the hydrogen (H+ )-ion activity in moles per liter
  Acid precipitation became a major environmental issue in the late 1970s and early 1980s in the industrial countries of the northern hemisphere.
  Naturally occurring precipitation is slightly acidic (pH of 5.6–5.7) because of the reaction of water with normal levels of atmospheric carbon dioxide (CO2)
  In the late 1970s and early 1980s the industrial countries of northeastern US and northern Europe experienced increasing acid rainfall pH values of 4.5 and 2.4 respectively, were reported.

## Slide 37
The increasing acidity of precipitation was caused by the atmospheric inputs of sulfur (S−) and nitrogen (N) oxides from the burning of fossil fuels such as coal and oil.
Of major concern are the impacts of acid deposition including both liquid and solid atmospheric particulates on aquatic and terrestrial ecosystems.
The effects of acid deposition are a global concern because of the long-range transport of acid by the atmosphere.
The impacts of acid deposition on streams and lakes are largely a function of the buffering capacity of soil surrounding them and the size of the watershed

## Slide 38
Acids become neutralized and waters may not become acidified if soils are alkaline or contain sufficient calcium (Ca).
However, lakes and streams that occur on infertile and shallow soils on top of acidic bedrock and have a low ratio of watershed area to water surface area are susceptible to acidification.
Fish and organisms providing their food are generally affected once the pH of streams and lakes drops below 6.0.
Acid deposition can inhibit bacterial decomposition and N fixation in the soil and can cause Ca, magnesium (Mg), and potassium (K) to be leached from the soil.
Controlling emissions such as sulfate (SO2) and nitrate (NOx) is the key to reducing acid precipitation.

## Slide 39
Atmospheric Deposition of Mercury
  One of the main sources of Hg to watersheds, streams, and lakes is by atmospheric deposition
  As a trace element in geologic formations, Hg is naturally released by the slow process of weathering though this process does not yield high concentrations to terrestrial and aquatic systems.
  However, there are several sources of Hg resulting from natural events and people’s activities in which Hg becomes volatile.
    Forest fires and volcanic eruptions expel Hg to the atmosphere.
    People’s activities including metal production, waste handling and treatment, and burning of fossil fuels, wood, and peat contribute to atmospheric Hg.

## Slide 40
Once in the atmosphere, Hg becomes widespread and has been found in remote wilderness areas.
Hg has a strong affinity for organic matter in soils and surface water.
As a result, Hg transport and cycling in a watershed is closely tied to the processes and movement of organic carbon.
Atmospheric Hg apparently accumulates on the forest canopy and reaches the soil which acts as a sink.

## Slide 41
PHYSICAL CHARACTERISTICS OF SURFACE WATER
  Among the more important physical characteristics of surface water that related to water quality are:
    suspended-sediment concentrations,
    bed-particle size,
    water temperature, and
    the level of dissolved oxygen (DO).

## Slide 42
Suspended Sediment
  The physical quality of naturally occurring surface water is determined largely by the amount of sediment that it carries.
  Of the two components (suspended and bedload), suspended sediment has a greater effect on water-quality because it restricts sunlight from reaching photosynthetic plants measured as turbidity
  sediment can carry undesirable concentrations of nutrients and heavy metals that affect water quality

## Slide 43
Sources of sediment
  An increase in the sediment load of streams is one of the most widespread causes of degradation in the quality of water from forest, woodland, rangeland, urban, and agricultural watersheds.
  Surface water from undisturbed forest watersheds has relatively low suspended sediment concentrations (generally < 20 ppm).
    While much of this sediment originates in the stream channel itself, sediment and/or from surface runoff during large storm events.
  Where organic soils are prevalent, much of the suspended material in streams is organic particles rather than mineral particles

## Slide 44
Higher concentrations of suspended sediment are often the result of accelerated erosion caused by disturbances in drainage areas such as
  timber-harvesting operations,
  overgrazing by livestock,
  road construction,
  agricultural cultivation,
  urban expansion,
  OR
  natural catastrophes including wildfires,
  large floods, and
  landslides.

## Slide 45
Nutrient and Heavy-Metal Transport Capacities of Sediment
  Nutrient and heavy-metal losses from upland watersheds are usually measured by dissolved ion concentrations.
  However, a potentially important source of nutrient and heavy-metal loss is through its transportation by sediment.
  Transported sediment from watersheds composed of different bedrock and vegetation combinations can carry high levels of nutrients and heavy metals.

## Slide 46
For example, a study of sediment from upland watersheds with limestone, granite, basalt, and sandstone geologies in the southwestern US shows that,
  limestone is high in Ca and K,
  basalt is high in sodium (Na).
  Mg is highest in the sand fraction of basalt and the clay-silt fraction of limestone
  While sandstone has the lowest concentration of these elements

## Slide 47
Variations in heavy-metal (zinc [Zn], iron [Fe], copper [Cu], manganese [Mn], lead [Pb], and cadmium [Cd]) levels in a stream are correlated with variations in sediment concentrations in many instances.
In the southwestern US, for example, sediment from different geologic strata has increasing heavy-metal concentrations in the following order:
  sandstone, granite, limestone, and basalt
From the standpoint of watershed management, land-use practices that increase sediment production can increase nutrient and heavy-metal movement with suspended sediment

## Slide 48
The nutrients adsorbed to sediment particles can be indicative of the type of geologic formation in an area.
Vegetation types on a watershed of a given geology primarily affect the organic matter content, total phosphorus (P), and levels of extractable nutrients of the sediments.
Sediment transport of P can reduce the chemical quality of surface waters and, as a consequence, result in substantial changes in aquatic ecosystems.
When P loading increases, eutrophication, that is, the process of nutrient enrichment leading to dense algae growth can be accelerated.
The resulting increase in algae and biomass in water systems can cause “dramatic adverse changes” in water quality.

## Slide 49
Thermal Pollution
  Water temperature can be a critical water-quality characteristic in many streams.
  The temperature of water, (the extremes) can control the survival of certain flora and fauna residing in a body of water.
  The type, quantity, and well-being of aquatic flora and fauna will frequently change with water temperature
  In general, an increase in water temperature causes an increase in the biological activity and places a greater demand on the dissolved oxygen (DO) in a water body.
  The solubility of oxygen in water is inversely related to temperature,
  Changes in water temperature can result in the replacement of existing species, such as cold-water spp being replaced by warm-water spp.

## Slide 50
Dissolved Oxygen
  The DO content in water has an effect on the aquatic organisms and chemical reactions that occur within the water body.
  The DO concentration of a water body is determined by the solubility of oxygen, which is inversely related to water temperature
  Relationship between the saturated solubility of oxygen in water and water temperature

## Slide 51
DO is a transient property that can fluctuate rapidly in time and space.
From a biological perspective, it is one of the most important water-quality characteristics in the aquatic environment.
DO concentration is typically measured continuously using an in situ sonde which captures diurnal variation.
A sonde is a multiparameter device that can hold several probes and make simultaneous measurements of parameters.
The sonde is a self-contained unit that can record and store data.
A commercially available sonde will include pH, specific conductance, and temperature; depending on the users’ need the sonde will also include DO, salinity, turbidity or oxidation reduction potential

## Slide 52
Dissolved chemical constituents
  Natural streams are part of the areas that they drain and, therefore, are an integral part of a watershed and its ecosystems.
  Water is an effective solvent and as it comes into contact with each part of the system, the chemical characteristics of the water adjust accordingly.
  Chemical reactions and physical processes often occur simultaneously as the water contacts the atmosphere, soil, and biota.
  It is these reactions and processes and the condition of each compartment of the ecosystem that determine the kind and amount of chemical constituents in solution.

## Slide 53
Streams that flow from undisturbed forested watersheds generally exhibit low concentrations of dissolved nutrients.
Because of this, the biological productivity in most of these streams is also low compared to intensively managed cropland watersheds where fertilizer applications add elements like N, P, and K to the soil.

## Slide 54
Sources of Nutrients
  The major sources of dissolved chemical constituents in streamflow are
    the constituents in the precipitation falling on the watershed,
    Geologic weathering of parent rock, and
    Biological inputs (primarily the photosynthetic production)
  Chemical and physical weathering then convert rock minerals into soluble or transportable forms that can be introduced into streams and lakes.
  Soils contribute the greatest amounts of dissolved chemical constituents to surface runoff and streamflow.
  As a result, land-use activities that affect soil properties and processes can affect the chemistry of streamflow.

## Slide 55
Some of the more important dissolved chemicals or nutrients that occur in surface waters are described as follows to aid in the understanding of the impacts of watershed management land use on water quality.

## Slide 56
Nitrogen
  Sources of N include
    the fixation of N gas by certain bacteria and plants,
    additions of organic matter to water bodies, and
    small amounts from the weathering of rocks.
  N occurs in several forms, including NH+4, gaseous NO, NO−2, and NO−3 .
  Organic N breaks down into NH+4, becomes oxidized to NO−3, available to plants.
  In the absence of oxygen, the process of denitrification can convert NO−3 back to NH+4 and N gas that typically escapes into the atmosphere.
  These are more considerable in croplands where large amounts of N fertilizers are applied

## Slide 57
NO−3 or NO3-N is an ion of considerable interest in relation to landuse & WM practices.
Streamflow from undisturbed forest lands usually contain lower concentrations of N and NO3-N than watersheds with Urban and agricultural development landuses
High concentrations of NO3-N in water can stimulate growth of algae and other aquatic plants but if P is present, only about 0.30 mg/L of NO3-N is needed for algal blooms.

## Slide 58
Phosphorus
  Sources of Phosphorus (P)
  Though less is known about the P cycle than the N cycle
    It originates from the weathering of igneous rocks,
    soil-leaching organic matter, and
    fertilizer inputs on intensively managed landscapes.
  In an aquatic environment, P becomes available to plants by weathering and is taken up and converted into organic P and upon decay, this process is reversed.
  However, along the way bio-available or soluble reactive P can fuel algae growth and reduce the transparency of lake water

## Slide 59
P mobility is mostly linked with both organic and inorganic sediments and can be buried and temporarily removed from the P cycle
Oxidation–reduction processes can also influence the binding and release of P into an open water system, for example, bonding by Fe compounds
P concentrations in streamflow are affected by land use just as N
Problems of eutrophication are often associated with accelerated loading of P to waters
Agricultural land use and urbanization result in the greatest problems of P loading to water bodies whereas P in wildland watersheds are typically low

## Slide 60
Calcium
  Calcium (Ca++) is one of the most abundant cations found in fresh waters because it is a major constituent of many rock types especially the carbonates such as limestone and dolomite.
  soluble Ca is intrinsically linked to CO2 present in soil water.
  Ca is one of the major ions contributing to hardness of water and specific conductance.
  High Ca concentrations do not appear to be harmful to fish and other aquatic life.
  Since Ca is typically present in most fresh-water environments, it can be used to infer the movement of water through a watershed.

## Slide 61
Magnesium
  Magnesium (Mg++) similar to Ca is abundant in carbonate rocks such as dolomite.
  Its solubility increases with greater concentrations of CO2 or a lower pH.
  The relationship between Ca and Mg can be helpful assessing water movement especially where open-water evaporation occurs within a watershed.
  Ca disassociates from CaCO−3 faster than Mg from minerals and this process will concentrate Mg in an open-water body such as a lake.
  The Ca:Mg ratio is approximately 4:1 or 3:1 in most carbonate-dominated geologic settings.
  Mg can be toxic to some fish in concentrations greater than 100–400 mg/L.
  High concentrations of Mg along with other ions limit aquatic life in arid or historically arid geologic settings.

## Slide 62
Sodium
  Abundant in both igneous and sedimentary rocks,
  sodium (Na+) is leached readily into surface and groundwater systems and remains in solution.
  Na is the cation most notably linked with common table salt (NaCl)
  Dissolved Na in most fresh water is typically low, so higher levels of Na in surface or groundwater may be from human sources.
  Na does not usually have any adverse impacts on fish unless both the Na concentration and the K concentration exceed 85 mg/L.
  Some levels of Na have beneficial effects by reducing the toxicity of aluminum and K salts to fish.

## Slide 63
Chloride
  Chloride (Cl−) is the most abundant of the halogens and combines with common metallic elements, such as alkali-earth metals that are readily soluble in water.
  Elevated concentrations of Cl, often associated with Na as described above, can be toxic to aquatic life.
  Therefore, it is of interest to be able to determine Cl concentrations in natural water bodies.

## Slide 64
Potassium
  Sources of potassium (K+) include igneous rocks, clays, and glacial material.
  K is usually less abundant than Na, but it is essential to plant growth and is recycled by aquatic vegetation.
  Pristine waters generally contain less than 1.5 mg/L of K, but nutrient-enriched or eutrophic waters can contain more than 5 mg/L.
  Fish kill can occur when K levels exceed 400 mg/L, while levels greater than 700 mg/L can kill invertebrates as well.
  Since K is used in large amounts on intensively managed agricultural cropland, they have high concentrations compared to wildland watersheds.

## Slide 65
Manganese
  Manganese (Mn++), found in igneous rocks, is leached from the soil.
  Mn is essential to plant metabolism and is circulated organically to become soluble upon decay.
  Concentrations of Mn rarely exceed 1mg/L in undisturbed waters unless associated with highly reduced waters typically found in a wetland.
  The drinking-water standard for Mn is 0.05 mg/L.
  The measurement of Mn and Fe++/Fe+++ in water is helpful for determining the relative oxidation state of a given sample of water.
  Elevated concentrations of Mn can suggest suboxic water which will not support fish because oxygen has been depleted.

## Slide 66
Sulfur
  Sulfur (S−) occurs naturally in water from the leaching of gypsum and anhydrite glacial soil igneous and sedimentary rocks.
  Weathering processes yield oxidized-sulfate (SO4−−) ions that are soluble in water.
  SO4−− is also found in rainfall at concentrations frequently exceeding 1-10mg/L
  The higher concentrations of atmospheric SO4−− are largely the result of air pollution and are the main contributors to acid precipitation.
  Water with desirable fish fauna generally contains less than 90 mg/L SO4−−
  Water with less than 0.5 mg/L will not support algal growth.
  Typical SO4−− drinking-water standards are 250 mg/L.

## Slide 67
Pesticides and Fertilizers
  Pesticides and fertilizers that are often used in agriculture and other land management have the potential to affect the quality of surface water and groundwater.
  These chemicals are introduced to accomplish management objectives by being applied to a specific target organism (pesticides) or location (fertilizers).
  Of concern to watershed managers are the chemicals that find their way into the water system and become transported to nontarget organisms.

## Slide 68
Toxicity effects can be either acute or chronic but are not necessarily lethal.
Acute effects are those caused by exposure to large doses of a chemical over a short period
Chronic effects are those caused by exposure to relatively small doses of a chemical over a long period.
Lethal: The concentration at which 50% of the organisms are killed is the lethal concentration (LC50) or the median tolerance limit (TLM).
Hence, one must realize that the characteristics of the chemical and the organism affected in addition to the size of the dose and the frequency and duration of contact all affect toxicity.

## Slide 69
Transport Processes
  Dissolved chemicals can leave a terrestrial system by
    subsurface flow through the soil,
    surface runoff, or
    groundwater.
  These processes are part of nutrient cycling, which consists of inputs, outputs, and movement of dissolved solids and gases within the system.
  Outputs of nutrients in streamflow from upland watersheds that are transported downstream can cause water pollution for downstream uses.
  Therefore, land use and the various factors that influence nutrient cycling and the chemistry of water leaving upland watersheds are frequently a concern.

## Slide 70
Movement of water through soil, along with the associated biological activity, controls the ionic composition of water leaving upland watersheds as streamflow.
The most chemically active components in soil are clays and organic colloids.
Because of their large surface areas per unit of volume and their negative electrical charge Clays have high exchange capacities.
Organic colloids also have a large capacity to exchange ions in solutions for those adsorbed on their surfaces.
A simplified concept of the exchange processes of clays and organic colloids is that adsorbed cations are exchanged selectively for H+ ions from the soil water.
The H+ ions, in turn, come principally from the solution of CO2 in water and the dissociation of the resulting H2CO3 molecule into two H+ ions and a bicarbonate ion.

## Slide 71
Ionic concentrations and their relationships to streamflow discharge are variable.
Ionic concentrations in large streams are commonly lower at times of high discharge than at low discharge largely due to the residence time of water in the soil.
Dilution also occurs when large volumes of water move through soils or as overland runoff and direct precipitation on the stream.
During periods of dry weather and low streamflow, the slow movement of water through soils enhances the opportunity for chemical reactions and soil-water concentrations of ions typically increase
Two of the fundamental controls on water chemistry in drainage basins are the type of geologic materials that are present and the length of time that water is in contact with those materials”

## Slide 72
BIOLOGICAL CHARACTERISTICS
  The two perspectives of biological characteristics of water bodies are:
    The occurrence of pathogenic organisms that impact human health,
      Bacteria and protozoa in water are two types of the more important pathogenic organisms affecting human health and
    The types and variety of biological organisms that can be used as indicators of the overall health of an aquatic ecosystem.
      The effects of pollution on a water body can ultimately be related to the types, variety, and amount of aquatic biota that exist in that water body.
  Therefore, biota can be used as indicators of surface-water quality and the overall habitat characteristics of aquatic ecosystems.

## Slide 73
Effects of sewage disposal on species composition and populations of higher aquatic life-forms in a stream (from Bartsch and Ingram, 1959

## Slide 74
GROUNDWATER QUALITY
  The usefulness of groundwater for drinking or irrigation depends largely on its quality, which is largely related to the type and location of the aquifer.
  Water from igneous and metamorphic rocks is generally of excellent quality for drinking exceptions occur in arid areas with high salts due to evaporation
  The quality of water in sedimentary rocks varies.
    Deep marine deposits can yield saline water but shallow sandstone and carbonate rocks can have good-quality water.

## Slide 75
Groundwater is generally of higher quality than surface water.
Because it is in direct contact with rocks and soil longer than most surface water,
groundwater is usually higher in dissolved mineral salts such as Na, Ca, Mg, and K cations with anions of Cl, SO4, and HCO3
If such salts exceed 1000 ppm (mg/L), the water is considered saline.

## Slide 76
Groundwater that contains high concentrations of Ca and Mg salts is defined as hard water.
Its hardness is determined by the solubility of calcite or its equivalent as follows:
  soft water, 60 mg/L;
  moderately hard, 61–120 mg/L;
  hard, 121–180 mg/L;
  very hard, more than 180 mg/L.
hard water does not represent health hazards but it is considered generally better for people’s health than soft water.