## Slide 1: Climate Change Mitigation Options in Waste Management Areas: Some Success stories and lessons from East Africa
Getinet Assabu (Ph.D.)
Debre Markos University ,
College of Agriculture and Natural Resources Department of Natural Resources Management

## Slide 2: Introduction
In past 200 years, Greenhouse has increased due to anthropogenic activities such as
Agricultural production
Industrial activities

## Slide 3
Production and use of fossil fuels

## Slide 4
Greenhouse gas emission from waste water treatment becomes a growing concern

## Slide 5: Cont’…
GHG emission from post-consumer waste and wastewater treatment represents approximately 3% of total global anthropogenic GHG emissions
methane represents 90% of waste sector emissions (Bogner et al., 2008).
Worldwide wastewater:-
  is the fifth largest source of anthropogenic CH4 emissions,
  contributing approximately 9% of total global CH4 emissions in 2000 (Bani Shahabadi et al. 2010).

## Slide 6
India, China, United States, and Indonesia combined account for 49% of the world‘s CH4 emissions from wastewater.
Global CH4 emissions from wastewater are expected to grow by approximately 20% between 2005 and 2020 (Gupta, 2012).

## Slide 7
2. Wastewater treatment process

## Slide 8
Resulting in significant challenges
Collection
Recycling
Treatment and Disposal

## Slide 11: Bar Screen
Catches large objects that have gotten into wastewater system such as bricks, bottles, pieces of wood, etc.

## Slide 12
Grit Chamber
- removes rocks, gravel, etc.

## Slide 13
Primary Treatment
  a physical process
  wastewater flow is slowed down and suspended solids settle to the bottom by gravity
  the material that settles is called sludge or biosolids

## Slide 14
Secondary treatment reduce further the suspended solids and B.O.D. of the wastewater.

## Slide 15
Methane
Carbon dioxide
Acetotrophic Methanogenesis
Hydrogenetrophic Methanogenesis
COMPLEX ORGANIC MATTER
Proteins
Carbohydrates
Lipids
Amino Acids, Sugars
Fatty Acids, Alcohols
hydrolysis
INTERMEDIARY PRODUCTS
(C>2; Propionate, Butyrate etc)
acidogenesis
Acetate
Hydrogen, Carbon dioxide
Homoacetogenesis
acetogenesis
2.1. Anaerobic Treatment
methanogenesis
1
1
1
1
1
2
3
5
4

## Slide 16
Common anaerobic treatment infrastructure includes anaerobic lagoons, conventional digesters, filter bed reactors, fluidized bed reactors, two stage digesters and high rate digesters such as the Upflow Anaerobic Sludge Bucket (UASB) design (Kurup, 2011).

## Slide 17: Anaerobic Contact Reactor
effluent
influent
sludge recycle
biogas
mixing

## Slide 18
Feeding
tank at 4oC
Biogas
Effluent
Peristaltic
pump
Media
Perforated
Al plate
Sampling
port
Heater
Constant temperature
recirculation line
Water
bath
Peristaltic pump
Sludge wastage
Upflow Anaerobic Filter

## Slide 19
Effluent
Influent
biogas
UASB Reactor

## Slide 23
Biogas
Sludge
Anaerobic baffled reactor
the wastewater passes overand under the baffles.

## Slide 24
Anaerobic Sequential Bach Reactor

## Slide 25
2.2. Aerobic Treatment
Convert OM to biomass and CO2.
Aerobic treatment is often used as part of a treatment train where digestate and residual material discharged from anaerobic systems undergo mechanical aeration (Kurup, 2011).

## Slide 26
2. 3. Biological Nutrient Removal
Biological nutrient removal (BNR);-
  to remove total nitrogen (TN) and
  total phosphorous (TP) from wastewater.
BNR process typically achieved via the following biological steps:

## Slide 27
1. Mineralisation/Ammonification;–
  organic compound conversion to inorganic ammonium;
2. Autotrophic nitrification;–
  oxidation of ammonium, primarily to nitrate and nitrite
3. Heterotrophic denitrification;–
  reduction of nitrate and nitrite to nitrogen under anoxic conditions

## Slide 28
  3. Greenhouse gas emissions
Wastewater treatment contribute to GHGs;-
Either through treatment processes or energy required for treatment
From the treatment process
    production of methane (CH4),
    nitrous oxide (N2O)
    carbon dioxide (CO2)
From Energy required for treatment
      carbon dioxide (CO2) (Cakir and Stenstrom, 2005).

## Slide 29
3. Sources of greenhouse gas emissions at WWTP
3.1 Methane (CH4) ;- occurs under anaerobic conditions
  Influent works;
  Anaerobic/anoxic tanks as part of activated sludge;
  and Sludge digestion and handling activities.

## Slide 30
3.2 Nitrous Oxide;-
The emission of N2O occurs;
  In the activated sludge units a
  grit tanks,
  pre-sedimentation secondary clarifiers,
  sludge storage tanks and
  anaerobic sludge digesters (Kampschreur et al., 2009).
N2O is a known intermediate of both nitrification and denitrification processes
N2O emissions from wastewater treatment have only recently been acknowledged in GHG emission methodologies.

## Slide 31
4. Strategies for Mitigation of GHG Emissions from Wastewater Treatment
Five key strategies which the wastewater treatment plants could adopt to reduce GHG emissions (Georges et al. 2009),.
1. Source Control:- extensive carbon savings may be accomplished through the control, at the source of priority pollutants of concern, thus avoiding the need for additional wastewater treatment.

## Slide 32
2. Least Carbon End-of-pipe/Process Addition:-
End-of-pipe treatment technologies:
  enhance the carbon content
  of the waste
  increase the operational needs
  for energy.
It is advisable to implement significant changes in the conventional approach to wastewater treatment to reduce significant carbon emissions.

## Slide 33
Greater Operational Efficiencies:-
  minimize higher energy demand
  enhances the operational efficiency of the system and reduces GHG emissions

## Slide 34
Redesigning of existing wastewater treatment system to
lower energy alternative

## Slide 35
5. Renewable Energy Generation:- This strategy aims at on-site energy generation, or generation within the wastewater treatment facility.

## Slide 36
5. Development of Integrated Process for Agro-process Waste Water Treatment and Renewable Energy Generation in East Africa

## Slide 37
5.1. Introduction
rapid expansion of agro-processing industries in Eastern Africa.
environmental degradation,
  discharge of untreated or partially treated wastewater
  greenhouse gas emissions,
  and consequently climate change.

## Slide 38
In addition, the current treatment processes do not integrate
    pollution reduction,
    Energy agro-process wastewaters.
    and nutrient recovery
Thus, they do not contribute to the energy supply or nutrient resources for improved agricultural productivity and climate change mitigation.

## Slide 39
This paves way;-
  for nutrient depletion from arable land,
  increased deforestation rates,
  increased GHG emissions
  and enhanced climate change.
To address these challenges and use the little available resources efficiently,
avoid duplication of efforts is necessary

## Slide 40
International/regional networking amongst expert scientists and private sector organizations in the region to develop and support appropriate technologies that mitigate climate change
  Addis Ababa University (Ethiopia),
  University of Dar Es Salam (Tanzania) and
  Makerere University (Uganda)
collaborative project to develop bioprocesses that produced biogas while treating the wastewater.

## Slide 41: Project Focus on
biogas production,
Slaughterhouse and banana wine process effluents in Uganda and Tanzania, respectively
Tannery effluents in Ethiopia,
biogas production,

## Slide 42
Goal:
Contribute to climate change mitigation, environmental sustainability, and agricultural development in Eastern Africa through integrated waste management innovation systems
Project outcomes
Pollution levels in water discharges at pilot test sites of partner countries in E. Africa reduced by up to 80%.
2) Biogas recovery, water and nutrient reuse from agro-process wastewater enhanced by 80% at partner pilot sites in Eastern Africa
3) GHG emissions from agro-process wastewater at pilot test sites of partner countries reduced by 80%

## Slide 43
Project outcomes
Pollution levels in water discharges at pilot test sites of partner countries in E. Africa reduced by up to 80%.
2) Biogas recovery, water and nutrient reuse from agro-process wastewater enhanced by 80% at partner pilot sites in Eastern Africa
3) GHG emissions from agro-process wastewater at pilot test sites of partner countries reduced by 80%

## Slide 44
Progress in Uganda

## Slide 46: Process cycle

## Slide 51
Progress in Tanzania

## Slide 52
Progress in
Ethiopia

## Slide 59
Challenges in the Ethiopian Component of the project;-
  Procurement system
  Bureaucratic nature of our system
  Understanding problem
  Lack of the necessary support for all concerned bodies including your minister