## Slide 1
Robot kinematics
Industrial Automation and Introduction to Robotics
Tesfaye M.
Industrial Control Engineering , SECE, DMiT.

## Slide 2: Robot kinematics
Robot arm kinematics deals with analytical study of the geometry of motion of robot arm with respect to a fixed reference coordinates system without regard to the forces/moments that cause the motion.
It is the study of geometric and time based quantities like position velocity and acceleration.
For a robot to perform a specific task the position and orientation of the end effector , its position and orientation relative to the base should be established first.
In particular we have to find the relationship between the joint variables and , position and orientation of the end effector of the robot arm.
For a manipulator, if the position and orientation of end effector are derived from the given joint angles and link parameters, this scheme is called forward kinematics.
On the hand the joint angles and the different configuration of the manipulator are derived from the position and orientation of the end effector is called inverse kinematics problem.
Forward kinematics
Inverse kinematics
Joint angles,
link parameters
Cartesian space(X,Y.Z)

## Slide 3: Cont.
For describing the position and orientation of the end effector and tool(for holding, welding ,and drill) with respect to the base frame it is imperative to know and formulate the body attached coordinate frame along the joint axis for each links in the manipulator chain of the robot.
So the relation between the body attached frame with the base frame of reference is described by transformation matrix
    Rotation(orientation) (3x3 matrix)
    Translation(position vector) (3x1 or 4x1 matrix)
Kinematics between two frame basically translation and rotation this relationship is represented by homogeneous transformation (4x4 matrix)

## Slide 4
Manipulator-type robots are multi degree-of-freedom (DOF), three dimensional, open-loop, chain mechanisms
The difference between open loop and closed-loop mechanisms

## Slide 5
A parallel mechanism

## Slide 6: Matrix representations
We use matrices to represent:
  Points (in space)
  Lines or vectors
  Objects
  Frames
  Movements (called transformations)

## Slide 7: Representation of a point in space
A point P in space can be represented by its three coordinates relative to a reference frame as:

## Slide 8: Representation of a vector in space
A vector can be represented by three coordinates of its tail and its head. If the vector starts at point A and ends at point B, then it can be represented by:

## Slide 9: Application of a scale factor
Makes the matrix 4 by 1
Allows for introducing directional cosines
  When , vector is actual length
  When , it represents an axis with its directional cosines

## Slide 10: The n-o-a frame designation
Approach, Orientation, Normal directions

## Slide 11: Representation of a frame relative to a fixed reference frame

## Slide 12: Representation of a rigid body (object)

## Slide 13: Frame representation requirements
The three unit vectors n, o, a are mutually perpendicular
Each unit vector’s length, represented by its directional cosines, must be equal to 1
These constraints translate into the following six constraint equations:
n.o=0 (the dot-product of n and o vectors must be zero)
n.a=0
a.o=0
(the magnitude of the length of the vector must be 1)
and

## Slide 14
The same can be achieved by:

## Slide 15: Homogeneous transformation matrices
4 by 4 matrices:
  Can be pre- or post-multiplied
  Easy to find inverse of the matrix
  Represents both orientation and position information, including directional axes

## Slide 16: Representation of transformations
A transformation may be in one of the following forms:
A pure translation
A pure rotation about an axis
A combination of translations and/or rotations

## Slide 17: Representation of a pure translation
Fnew = Trans (dx ,dy ,dz )
Fold

## Slide 18: Representation of a pure rotation about an axis

## Slide 19: Rotation matrices

## Slide 20: Representation of combined transformations
Example:
Rotation of degrees about the x-axis,
Followed by a translation of [l1,l2,l3] (relative to the x-, y-, and z-axes respectively),
Followed by a rotation of degrees about the y-axis.
Pre-multiply by each matrix:

## Slide 21: Transformations relative to the current rotating frame
In this case, matrices representing each transformation are post-multiplied.
If transformations are relative to both the Universe frame and the current frame, each matrix is accordingly multiplied, either pre- or post-.

## Slide 22: Relationship between frames

## Slide 23: Inverse of matrices
The following steps must be taken to calculate the inverse of a square matrix:
  Calculate the determinant of the matrix.
  Transpose the matrix.
  Replace each element of the transposed matrix by its own minor (adjoint matrix).
  Divide the converted matrix by the determinant.

## Slide 24: Inverse of rotation matrices
The inverse of a rotation matrix is its transpose because rotation matrices are “unitary”.

## Slide 25: Inverse of transformation matrices
The inverse of a transformation (or a frame) matrix is the following:
  1. Transpose the rotation portion of the matrix.
  2. Take the negative of the dot-product of the p and n, p and o, and p and a vectors.
  The scale factors remain the same.

## Slide 26: Forward and inverse kinematic equations
Forward kinematics includes substituting the known joint values into the equations to find the location and orientation
Inverse kinematics includes finding an equation that results in joint values if the desired position and orientation are specified.

## Slide 27: Forward and inverse kinematics for positioning
Four possibilities are common:
  a. Cartesian (gantry, rectangular) coordinates
  b. Cylindrical coordinates
  c. Spherical coordinates
  d. Articulated (anthropomorphic or all-revolute) coordinates

## Slide 28: Cartesian coordinates
Three linear motions.

## Slide 29: Cylindrical coordinates
Two linear and one revolute joints

## Slide 30: Inverse solution
Use the position equations to find the joint values.
The application of ATAN2 function for correct determination of angles.

## Slide 31: Spherical coordinates
Two revolute and one linear joints

## Slide 32: Inverse solution
Use the position equations to determine the joint values.
Check your answers for correct values.

## Slide 33: Articulated coordinates
We will study later with the Denavit–Hartenberg methodology

## Slide 34: Forward and inverse kinematics for orientation
Three possibilities are common:
  a. Roll-pitch-yaw (RPY) angles
  b. Euler angles
  c. Articulated coordinates

## Slide 35: RPY angles

## Slide 36: Inverse solution
Use:

## Slide 37: Euler angles

## Slide 38: Inverse solution
Use:

## Slide 39: Articulated angles
We will study later with the Denavit–Hartenberg methodology

## Slide 40: Combination of different formats
Multiply the transformations as appropriate:

## Slide 41: Denavit-Hartenberg (DH) representation of forward kinematic equations of robots
May be used for any configuration, whether specific coordinates or not.
Can include joint offset, twist angles, multi-variable joints, and so on.
Very common.
Many other equations are based on this methodology

## Slide 42: D-H representation

## Slide 43: D-H representation
z-axes always along the joint motion.
θ represents joint rotation.
d is joint linear displacement or distance between common normals.
α is the twist angle between z-axes.
a is the length of the common normal.

## Slide 44: D-H representation: what to do
Assign z-axes to each joint along linear motion or revolute axis.
Assign x-axes along the common normal between successive z-axes.
No need for y-axes.
If z-axes coincide, x-axis is perpendicular to both.
If z-axes are parallel, x-axes can be anywhere.

## Slide 45: D-H local transformations
Four transformations are necessary to go from one frame to the next:

## Slide 46: D-H local transformations
Rotate about the zn-axis an angle of . This will make xn and xn+1 parallel to each other. This is true because an and an+1 are both perpendicular to zn, and rotating zn an angle of will make them parallel (coplanar).
Translate along the zn-axis a distance of dn+1 to make xn and xn+1 colinear. Since xn and xn+1 were already parallel and normal to zn, moving along zn will lay them over each other.
Translate along the (already rotated) xn-axis a distance of an+1 to bring the origins of xn and xn+1 together. At this point, the origins of the two reference frames will be at the same location.
Rotate zn-axis about xn+1-axis an angle of to align zn-axis with zn+1-axis. At this point, frames n and n+1 will be exactly the same, and we have transformed from one to the next.

## Slide 47: D-H representation
A transformation matrix can be formed by:

## Slide 48: D-H representation
An A-matrix is:

## Slide 49: Total transformation
The total transformation between the base and the end of the robot is:

## Slide 50: D-H representation
A parameters table may look like:

## Slide 51: D-H representation
Example: A simple 6-axis robot

## Slide 52: Parameters table

## Slide 53: Inverse kinematic equations
Find a set of equations that allow determination of joint values from desired position and orientation information.
Each robot has a different solution.
It may be necessary to use different approaches for each robot.
This usually requires pre-multiplication of transformation matrices by inverse of individual A matrices, squaring of terms, divisions, and so on.

## Slide 54: Inverse kinematic equations
The total transformation is:

## Slide 55: Inverse kinematic equations
For the shown example, the following may be found:
  where and

## Slide 56: Inverse kinematic equations: cont.

## Slide 57: Inverse kinematic programming of robots

## Slide 58: Dual-arm cooperating robots
Robots that work together or robots with two arms.
Courtesy of Yaskawa Electric.

## Slide 59
Loop equations:

## Slide 60: Degeneracy
When a degree of freedom is lost.

## Slide 61: Dexterity
When a position within the work envelope can be specified, but orientation is limited. This usually happens near the boundaries or reach.

## Slide 62: The fundamental problem with the Denavit-Hartenberg representation
No transformation along the y-axis is allowed.
Manufacturing errors in joints are usually in this direction.

## Slide 63: Reference
INTRODUCTION TO ROBOTICS ANALYSIS, CONTROL, APPLICATIONS Second Edition,Saeed Benjamin Niku,