## Slide 1
ACTUATORS AND DRIVE SYSTEMS
Industrial Automation and Introduction to Robotics
Tesfaye M.
Industrial Control Engineering , SECE, DMiT.

## Slide 2: Introduction
The following types of actuators will be discussed:
Electric motors
  Servomotors
  Stepper motors
  Direct drive electric motors
Hydraulic actuators
Pneumatic actuators
Novelty actuators
Other issues

## Slide 3: Characteristics of Actuating Systems
Common characteristics include:
  Nominal characteristics such as power-to-weight ratio, and other specifications,
  Stiffness versus compliance,
  Gear reduction.

## Slide 4: Power-to-Weight Ratio
Highest for hydraulic system
  If all components are included, not the highest.
  Power units are heavy, actuators are relatively lighter.
Medium range for electric motors (except steppers).
Lowest for pneumatic systems.

## Slide 5: Stiffness Versus Compliance
Stiff systems are more responsive and more accurate
They do not deform easily; can cause damage to themselves or to other systems.
May need selective compliance.

## Slide 6: Use of Reduction Gears
Hydraulic system do not require it; electric systems require gear reduction (except in direct drive systems).
Gear reduction results in:
  Increased number of parts, higher weight, more cost.
  Increased backlash, more space requirement.
  More noise, more inertia, more complications.
  Decreased inertial load on actuators by a factor of:

## Slide 7: Comparison of Actuating Systems: Hydraulic
+ Good for large robots and heavy payload
+ Highest power/weight ratio
+ Stiff system, high accuracy, better response
+ No reduction gear needed
+ Can work in wide range of speeds without difficulty
+ Can be left in position without any damage
- May leak; not fit for clean room applications
- Requires pump, reservoir, motor, hoses, and so on
- Can be expensive and noisy; requires maintenance
- Viscosity of oil changes with temperature
- Very susceptible to dirt and other foreign material in oil
- Low compliance
- High torque, high pressure, large inertia on the actuator

## Slide 8: Comparison of Actuating Systems: Electric
+ Good for all sizes of robots
+ Better control, good for high precision robots
+ Higher compliance than hydraulics
+ Reduction gears reduce inertia on the motor
+ Do not leak, good for clean room
+ Reliable, low maintenance
+ Can be spark-free. Good for explosive environments
- Low stiffness
- Need reduction gears, increased backlash, cost, weight, and so on
- Motor needs braking device when not powered; otherwise, the arm may fall.

## Slide 9: Comparison of Actuating Systems: Pneumatic
+ Many components are usually off-the-shelf
+ Reliable components
+ No leaks or sparks
+ Inexpensive and simple
+ Low pressure compared to hydraulics
+ Good for on-off applications and for pick and place
+ Compliant systems
- Noisy
- Require pressurized air, filter, and so on
- Difficult to control their linear position
- Deform under load constantly
- Very low stiffness, inaccurate response
- Lowest power to weight ratio

## Slide 10: Hydraulic Actuators
Powerful systems. The force developed is:
In rotary systems, the torque is:
The flow rate needed is:

## Slide 11: Components of Hydraulic Systems
A hydraulic system consists of:
Hydraulic linear or rotary actuator.
Hydraulic pump.
Electric motor or an engine.
Cooling system.
Reservoir.
Accumulators.
Servovalves.
Check-valves.
Holding valves.
Connecting hoses.
Filtering system.
Sensors.

## Slide 12: Schematic of a Hydraulic System

## Slide 13: Pneumatic Devices
Very similar to hydraulic systems.
Pressurized air is used.
Lower working pressures mean lower power-to-weight ratio.
Air is compressible; hard to control.
Used for insertion purposes and ½-DOF actuation
Simple, rugged, inexpensive, safe.
Leakage is not a problem even in clean room.

## Slide 14: Electric Motors
There are many types of electric motors.
AC, DC, Stepper motors, direct drive motors, brushless DC motors are discussed here.
Electromotive Force (emf) concept:
  In the presence of a magnetic field, a conductor carrying a current experiences a force.
  In the presence of a changing magnetic field or when a conductor crosses a field, a voltage is induced in it (called back-emf).

## Slide 15: Fundamental Differences between AC and DC-Type Motors
Speed control
  DC motor speed can be controlled by changing voltage (or current).
  AC motor speed is a function of line frequency.
Brushed versus brushless
  Brushless motors are simpler and last longer
Heat dissipation
  AC-type motors dissipate heat more efficiently
  They can work with higher currents without damage

## Slide 16: Heat Dissipation Path
In a DC-type motor heat is generated in the rotor.
  Heat must pass through the air gap, permanent magnets, body of the motor.
In an AC-type motor, heat is generated in the stators.
  Heat must pass through the magnets, and body of the motor.

## Slide 17: Heat Generation in Motors
Heat generation is a function of the following parameters:
The basic heat generated in the winding.
As the winding heats up, resistance increases, further increasing heat generation.

## Slide 18: Heat Generation in Motors: Cont.
The strength of the magnetic flux is negatively affected by heat, reducing the torque and requiring additional current.
Heat dissipation increases as temperature rises.

## Slide 19: DC Motors
Are very common in industry
They are reliable, sturdy, and relatively powerful.
The stator is a set of permanent magnets
Rotor carries the current
Brushes and commutators are used to change the polarity for continued rotation.

## Slide 20: DC Motors: Cont.
The governing equation for DC motors is
The output power of the motor is zero when
1. The angular velocity of the motor (at stall condition)
2. The torque is zero (at maximum speed)

## Slide 21: Low Inertia DC Motors Pictures courtesy of Automation Source Technologies and Printed Motor Works Ltd, UK

## Slide 22: Frameless Motors
These motors can be directly integrated into the structure of the joint. Similar gear reduction can be used for proper rotational speed and torque requirements.
Courtesy of Maxon Precision Motors.

## Slide 23: AC Motors
The rotor is permanent magnet or a cage
The stator houses the windings
No brushes or commutators
Changing flux is provided by the AC current
Speed is a function of line frequency (in synchronous motors)
Can dissipate heat more favorably than DC motors; more powerful
Reversible AC motors work with center-tapping as shown.

## Slide 24: Brushless DC Motors
A hybrid between AC motors and DC motors.
Three sets of electromagnets used, 120 degrees apart.
Rotor is permanent magnet with multiple poles.
Feedback is necessary to electronically switch the direction of the current.
Each coil is energized when the rotor reaches a specific location.
The location is sensed by Hall-effect sensors or similar.
Speed can be controlled, a DC motor, but behaves like an AC motor.

## Slide 25: Direct Drive Electric Motors
Very similar in construction to brushless DC or stepper motors.
They deliver a very large torque at very low speeds with very high resolution.
A voice coil may be used as a direct drive actuator for low torque but high resolution applications.

## Slide 26: Servomotors
As speed of the rotor increases so does back-emf at
At nominal no-load speed the back-emf current is equal to the supplied current.
When a load is applied the speed decreases to reduce back-emf current, therefore creating a net torque.
In servomotors, the speed is measured and voltage (current) is adjusted to achieve the desired speed.
Feedback is also used to measure rotational position and stop the motor when destination is reached.

## Slide 27: Servomotors: Cont.
Figures show this relationship:
Servomotor schematic:

## Slide 28: Stepper Motors
Stepper motors are versatile, robust, and simple motors.
They require a drive circuitry, but no feedback.
Each step provides a known angle of motion.
Unless a step is missed, speed and positional control is easy.
They come in many different forms and principles of operation.
Stepper motors have soft iron or PM rotors.
Their stators house multiple windings.
Construction is similar to AC-type motors.

## Slide 29: Stepper motors: Canstack
Principle of operation:
  Full step
  ½ step

## Slide 30: Canstack Motors
The rotor:
Alternate N, S poles, made based on Halbach array.

## Slide 31: Canstack Motors: Cont.
The stator is made up of four plates with tabs (poles) staggered in 1-3-2-4 pattern as shown.
  Each coils makes one of the plates all N or all S poles.
  Alternate coils create alternate (rotating) flux patterns.

## Slide 32: Canstack Motors: Cont.
During operation, two coils will be turned on in the following sequence resulting in the indicated polarities:

## Slide 33: Canstack Motors: Cont.
The result is the following rotating patterns (each arc is one sequence).
Each sequence rotates the rotor one step.

## Slide 34: Canstack Motors: Cont.
Half-stepping can be done as follows:

## Slide 35: Hybrid Stepper Motors
Usually made with two coils, center tapped, or two independent windings in opposite directions, each with four poles.
PM rotor is made of two collinear cylinders, one end is north, other end is south
The rotor and the stator poles are all cut to have teeth; the teeth on one half of the rotor are offset by a half tooth from the other half of the rotor.

## Slide 36: Hybrid Stepper Motors: Cont.
Calipers: Principle of work
  Can measure very small distances.
  Same principle is used for small step angles in a stepper motor.

## Slide 37: Hybrid Stepper Motor: Cont.
A similar sequence of switchings as in canstack motors causes a rotating flux.
The rotor follows the flux at small angles.
Controlling how many switchings, and how fast, determines angle of rotation and speed.

## Slide 38: Unipolar, Bipolar, and Bifilar Stepper Motors
Unipolar motors require one power source.
  Generally impossible to run in ½ steps
  Motor develops full power.
Bipolar motors require power-source polarity change or two power sources
  Can be run in full or ½ step modes.
  Motor develops full power.
In bifilar motors, the coils are center-tapped.
  One power source needed.
  Can be run in full or ½ step modes.
  Motor develops ½ power.

## Slide 39: Stepper Motor Wiring Configurations

## Slide 40: Torque-Speed Characteristics
Maximum torque, called holding torque, is developed at zero angular velocity
As the speed increases, the torque it develops decreases significantly due to:
  Inertial load: At higher speeds, the rotor must accelerate, cruise, decelerate, and stop at each step.
  Back-emf caused by the alternating magnetic field of the stator pulls back the rotor, slowing it.

## Slide 41: Torque-Speed Characteristics: Cont.
To remedy:
Diodes may be used to stop the back-emf current.
Zener diodes improve the performance because of their higher breakdown voltage.
Microstepping decreases stop-and-go inertial load, increasing performance and speed.

## Slide 42: Micro-stepping
Instead of fully-on and fully-off switching, each coil is switched on and off in many steps.
128, 256, 512, etc. steps per step are common.
50,000 steps per revolution is common.
Many different patterns for switching is used.
A sinusoidal pattern creates an AC motor with controlled speed and positional control.

## Slide 43: Stepper Motor Control
Microprocessors or similar dedicated circuits are used.
Four output ports can be used to run one stepper at full control.
Power transistors needed if the output is low current.

## Slide 44: Stepper Motor Control: Cont.
Dedicated stepper drivers may be used as well.
Only two ports are needed to run a stepper with full control:
  One signal needed for stepping, one for direction control.
  The drive signal is a simple stream of impulses.

## Slide 45: Microprocessor Control of Electric Motors
Many bits (output ports) needed for full speed control
  Pulse width modulation is used
Changing polarity is difficult
  H-Bridge can be used

## Slide 46: Transistor Power Output
Transistors are most efficient when run at full power.
Power is lost and heat generated at other values.

## Slide 47: Pulse Width Modulation
Instead of changing the actual value of voltage, the average value is varied by changing the time the signal is on and off.
As long as the number of switchings is many times the natural frequency of the rotor, no vibration is felt.
Since transistors are fully on or off, little power is lost.
Sinusoidal output can be created as well.

## Slide 48: Direction Control by H-Bridge
Direction of current can be changed using two microprocessor output ports.
Motor can be freewheeling, move in either direction, or braked.
Care must be taken to never have same side transistors on together.

## Slide 49: H-bridge Control
Microprocessor control of an H-bridge

## Slide 50: Other Actuators
Magnetostrictive Actuators
Shape-Memory Type Metals
  Titanium-Nickel alloy, called Biometal™ (muscle wire)
Electroactive Polymer Actuators (EAP)

## Slide 51: Speed Reduction

## Slide 52: Speed reduction: Cont.

## Slide 53: Speed Reduction: Cont.
In Harmonic drives a flexspline gear is used to overcome interference between gears.
Printed with permission from Harmonic drive, LLC. “Harmonic Drive” is a trademark of Harmonic Drive LLC