## Slide 1
Debre Markos University
ደብረ ማርቆስ ዩኒቨርስቲ
Debre Markos Institute of Technology
ደብረ ማርቆስ ቴክኖሎጂ ኢንስቲትዩት
School of Electrical and Computer Engineering
Mechanism and Actuation
Industrial Automation and Introduction to Robotics
Tesfaye M.
Industrial Control Engineering , SECE, DMiT.

## Slide 2: Mechanism and Actuation
The Robot Design
Early robots were designed with general motion capability under the assumption that they would find the largest market if they could perform the widest variety of tasks;
This emphasis on flexibility proved to be expensive in both cost and performance.
Robots are now beginning to be designed with a specific set of tasks in mind.
Robot design focuses on the number of joints, physical size, payload capacity, and the movement requirements of the end-effector.
The configuration of movable skeletons and overall size of the robot is determined by the task requirement, workspace, and reorientation ability.
A critical concern in robotic system design is the range of tasks the robot is expected to perform.
The robot should be designed to have the flexibility it needs to perform the range of tasks for which it is intended

## Slide 3
This determines the topology of the robot mechanism and the actuator system.
The choices of geometry, material, sensors, and cable routing follow from these basic decisions.
The robot control algorithms must control the vibration of the system as well its gross motion.
industrial robot are worked with other piece of equipment such as conveyors, production machines, and other tools with human
Robot and this equipment's forms workspace/workstation
Robot application engineer must consider the physical design of workstation and the design of robot control system.
During design of robot system
Mechanical structure system
Actuator system
Mechanism and Actuation

## Slide 4
Parts of robotic system
Mechanical structure of robot is like skeleton of human body
The mechanical structure of the robot is also called manipulator structure
The manipulator is made up of a series of segments and joints much like those found in the human arm.
manipulator is the arm of the robot which must move materials, parts, tools, or special devices through various motions to provide useful work.
( Manipulator structure) (Reis Machines, Inc.)
Mechanism and Actuation

## Slide 5
Mechanical Structure
Mechanical structure is a physical structure of the robots such as beams, links, slides, joints, and bearings of a robot that create a movable skeleton.
This skeleton of robots, the mechanical structure, is also known as mechanism of the robot.
Mechanical structure of manipulator(robotic arm) consist of
Links(rigid parts)
Joints
Arm
wrist
End-effector
Mechanism and Actuation

## Slide 6
Links
For the purposes of dynamic modeling, the links of a robot are generally considered to be rigid. However, a robot is not a rigid structure.
Like all structures it deflects under applied loads, such as its own weight and the weight of the payload, termed gravity loading;
For industrial robots a critical concern is the link stiffness in bending and in torsion.
To provide this stiffness, robot links are designed either as beams or shell (monocoque) structures.
Monocoque structures have lower weight or higher strength-to-weight ratios, but are more costly and generally more difficult to manufacture.
Cast, extruded, or machined beam-based links are often more cost effective;
Mechanism and Actuation

## Slide 7
Two rigid binary link in free space a chain formed by joining two links
Two links 1 and 2,each has two holes at the end.
This two links are connected by joint, by put a pin through holes(B&C)
Links are formed by straight lines with rotary joints (small circle)
The joint formed is called pin joint/revolute/rotary joint
Mechanism and Actuation Links…

## Slide 8
Joints
Joints are a part of robot skeleton that enable it perform several motions.
The robot joint mechanism is a source of the robot flexibility and consists at least four major elements: 1) the joint axis structure 2) an actuators 3) transmissions and 4) state sensors, force sensor
The sensors are usually incorporated in the joint mechanism to measure position, velocity, and force feedback for the controller.
Many types of joints can be made between two links.
For instance, the rotary and linear movements of robots are achieved by means of revolute and prismatic joints respectively.
The most common joints are: Revolute, Prismatic, Screw, Ball-in-socket and Hook-type universal joints.
Mechanism and Actuation

## Slide 9
Types of joint
Revolute joint prismatic joint
Spherical joint universal joint
Mechanism and Actuation

## Slide 10
Prismatic joints
It is know as sliding as well as linear joints.
Most cross sectional of the joint is considered as generalized “prism”
It permits links to move in linear relationship
The joint motion is defined by sliding or translational mov’t of the links
Rotational joints
The two links are jointed by a pin/pivot about the axis of which the links can rotate with respect to each other
Other types of possible joints are planar, cylindrical and spherical etc.…
Mechanism and Actuation

## Slide 11
End effector
It is attached to the wrist of robot arm and enables the general purpose of the robot to perform a specific task.
It is sometimes referred to as ‘’hand”
It is used for grasp and hold objects.
Catons, bottles, raw materials, and tools are handled by robot end effctor
Mechanism and Actuation

## Slide 12
Actuators
Actuators supply the motive power for robots.
Most robot actuators are commercially available components, which are adapted or modified, as necessary, for a specific robot application.
The actuators are a source of force or torque that cause the links of mechanism to move.
The most common actuators includes: motors, hydraulic and pneumatic pistons, and other elements that generate a mechanical force.
The actuators with mechanism enable a robot to transform a set of computer commands into versatile physical movements.
The three commonly used actuators are hydraulic, pneumatic, and electromagnetic.
Electrical actuators use electric power.
Pneumatic actuators use pneumatic (air) power.
Hydraulic actuators use hydraulic (fluid) power.
Mechanism and Actuation

## Slide 13
Ac servo motors, dc servo motors, and stepper motors are most common electrical actuators.
Both ac and dc servo motors have built-in methods for controlling exact position.
Stepper motor gives precise position with out sensor.
It is transforms incoming electrical pulses into equal increments of rotary shaft motion(steps)
Other basic parts of robotics system
  Controllers(microcontrollers, software algorism's, Electronic Hardware )
  Sensors
Mechanism and Actuation

## Slide 14: Mechanism and Actuation
Degree of freedom for s system(DOF)
It is define as one of the variables(most of the time six) requires to define the motion of the body in space
DOF of a system depends on the number of variables/coordinates that are needed to describe its position
the degrees of freedom of robotic system is defined as the minimum number of independent parameters, variables, or coordinates needed to describe a robotic system completely
Each joint in a robotics system gives the robot one DOF
Six DOF needed for complete control over positioning and orientation
Fewer DOF is possible
Many robots have fewer than 6 DOF
More DOF is impossible to solve unless new constraint equations or optimization routines are applied

## Slide 15: Mechanism and Actuation
Robot coordinates
Industrial robot are available in a wide variety of sizes, shapes, and physical configurations
This common coordinates are
cartesian
Polar
Cylindrical
Spherical….etc.

## Slide 16
Cartesian coordinates(X,Y,Z)
Cylindrical coordinates
Mechanism and Actuation

## Slide 17
Spherical robot
See by your self the following configuration!!!
Articulated configuration
SCARA(Selective Compliance Assembly Robot Arm)
Mechanism and Actuation

## Slide 18: THANK YOU!!!