## Slide 1: CHAPTER- 4
4. SOIL CHEMISTRY
4.1. Soil and agriculture
Cultivation of land and agricultural practices can influence both the atmosphere and the hydrosphere.
Agriculture can be divided into the two main categories of crop farming, in which plant photosynthesis is used to produce grain, fruit, and fiber, and livestock farming, in which domesticated animals are grown for animal Products.
Often quite different from either parent strain, hybrids tend to exhibit “hybrid vigor” and to have significantly higher yields.

## Slide 2: Cont…
The rearing of domestic animals may have significant environmental effects.
Its byproducts have caused serious problems.
Hog production caused very damaging water pollution.
An interesting aspect of the problem is emission of greenhouse-gas methane by anaerobic bacteria in the digestive systems of animals.
Soil, consisting of a finely divided layer of weathered minerals and organic matter upon which plants grow, is the most fundamental requirement for agriculture.

## Slide 3: Cont…
Soil is the receptor of large quantities of pollutants, such as particulate matter from power plant smokestacks.
Fertilizers, pesticides and some other materials applied to soil often contribute to water and air pollution.
Soil is a key component of environmental chemical cycles.
Soils are formed by the weathering of parent rocks as the result of interactive geological, hydrological, and biological processes.
Soils are porous and are vertically stratified into horizons as the result of downward-percolating water and biological processes, including the production and decay of biomass.
Soils are open systems that undergo continual exchange of matter and energy with the atmosphere, hydrosphere, and biosphere.

## Slide 4: 4.2. Nature and composition of soil
Soil is a variable mixture of minerals, organic matter, and water.
It is the final product of the weathering action of physical, chemical and biological processes on rocks, which largely produces clay minerals.
The organic portion of soil consists of plant biomass in various stages of decay.
High populations of bacteria, fungi, and animals such as earthworms may be found in soil.
Soil contains air spaces and generally has a loose texture.

## Slide 5: Cont…
The solid fraction of typical productive soil is approximately 5% organic matter and 95% inorganic matter.
Some soils, such as peat soils, may contain as much as 95% organic material.
Other soils contain as little as 1% organic matter.
Biological processes, such as bacterial decay of residual plant biomass, produces slightly acidic CO2, organic acids, and complexing compounds that are carried by rainwater to lower horizons where they interact with clays and other minerals, altering the properties of the minerals.
The top layer of soil, typically several inches in thickness, is known as the A horizon, or topsoil.

## Slide 6: Cont…
This is the layer of maximum biological activity in the soil and contains most of the soil organic matter.
Metal ions and clay particles in the A horizon are subject to considerable leaching.
The next layer is the B horizon, or subsoil.
It receives material such as organic matter, salts, and clay particles leached from the topsoil.
The C horizon is composed of weathered parent rocks from which the soil originated.

## Slide 7: Cont…
Soils characteristic classification depend on its purposes, including crop production, road construction, and waste disposal.
The parent rocks from which soils are formed obviously play a strong role in determining the composition of soils.
Other soil characteristics include strength, workability, soil particle size, permeability, and degree of maturity.
One of the more important classes of productive soils is the type of soil formed under relatively high rainfall conditions in temperate zones of the world.

## Slide 8: Cont…
These rich soils tend to be acidic (pH 3.5–4.5) such that alkali and alkaline earth metals and, to a lesser extent aluminum and iron, are leached from their A horizons, leaving kaolinite as the predominant clay mineral.
At somewhat higher pH in the B horizons, hydrated iron oxides and clays are redeposited.
According to the United Classification System (UCS), four major categories of soil particle sizes are : Gravels (2–60 mm) > sands (0.06–2 mm) > silts (0.06-0.006 mm) > clays (less than 0.002 mm).

## Slide 9: Water and Air in Soil
Water is part of the three phase, system making up soil.
It is the basic transport medium for carrying essential plant nutrients from soil to plant roots and to the plant parts.
Water held in smaller pores or between the unit layers of clay particles is held much more strongly.
Soils high in organic matter may hold appreciably more water than other soils, but it is relatively less available to plants because of physical and chemical sorption of the water by the organic matter.
There is a very strong interaction between clays and water in soil.

## Slide 10: Cont…
Water is absorbed on the surfaces of clay particles.
Because of the high surface/volume ratio of colloidal clay particles, a great deal of water may be bound in this manner.
In water saturated soil (waterlogged) oxygen rapidly used up by the respiration of microorganisms that degrade soil organic matter.
Most crops, exception rice, cannot grow on waterlogged soils.
The most marked chemical effects of waterlogging is a reduction of pE by the action of organic reducing agents (bacteria).

## Slide 11: Cont…
One of the more significant results of this change is the mobilization of iron and manganese as soluble iron(II) and manganese(II) through reduction of their insoluble higher oxides:
Some soluble metal ions such as Fe2+ and Mn2+ are toxic to plants at high levels.
Their oxidation to insoluble oxides may cause formation of deposits of Fe2O3 and MnO2, which clog tile drains in fields.
Roughly 35% of the volume of typical soil is composed of air-filled pores.

## Slide 12: Cont…
Whereas the normal dry atmosphere at sea level contains 21% O2 and 0.03% CO2 by volume, these percentages may be quite different in soil air because of the decay of organic matter:
(CH2O) + O2 → CO2 +H2O
This process consumes oxygen and produces CO2. Due to this oxygen content in soil may be as low as 15%, CO2 content may be several percent.
This lowers the pH and contributes to weathering of carbonate minerals, particularly calcium carbonate:
CaCO3(s) + CO2 + H2O ↔ Ca2++ 2HCO3−

## Slide 13: 4.3. Nutrients in soil
Nutrients of soil may be organic or inorganic.
Inorganic soil colloids often absorb toxic substances in soil, thus playing a role in detoxification of substances that otherwise would harm plants.
The abundance and nature of inorganic colloidal material in soil are obviously important factors in determining soil productivity.
The most common elements in the earth‘s crust are oxygen, silicon, aluminum, iron, calcium, sodium, potassium, and magnesium.
From these elements particularly silicon and oxygen constitutes most of the mineral fraction of the soil.

## Slide 14: Cont…
Common soil mineral constituents are finely divided quartz (SiO2), orthoclase (KAlSi3O8), albite (NaAlSi2O2), epidote (4CaO•3(AlFe) 2O3•6SiO2•H2O), geothite (FeO(OH)), magnetite (Fe3O4), calcium and magnesium carbonates (CaCO3, CaCO3•MgCO3), and oxides of manganese and titanium.
Though less than 5% of a productive soil, organic matter largely determines soil productivity.
Some organic compounds even contribute to the weathering of mineral matter, the process by which soil is formed, Eg, C2O42−
Where M is Al or Fe.

## Slide 15: Cont…
Some soil fungi produce citric acid and other chelating organic acids which react with silicate minerals and release potassium and other metal ions.
Biologically active organic soil fraction includes polysaccharides, amino sugars, nucleotides, and organic sulfur and phosphorus compounds.
Humus, a water-insoluble material that biodegrades very slowly, makes up the bulk of soil organic matter.
The accumulation of organic matter in soil is strongly influenced by temperature and availability of oxygen.

## Slide 16: Cont…
The rate of biodegradation decreases with decreasing temperature, organic matter does not degrade rapidly in colder climates.
The organic content may reach 90% in areas where plants grow and decay in soil saturated with water.
The presence of naturally occurring polynuclear aromatic (PAH) compounds is an interesting feature of soil organic matter.
Terpenes also occur in soil organic matter.

## Slide 17: The Soil Solution
The soil solution is the aqueous portion of soil that contains dissolved matter from soil chemical and biochemical processes in soil and from exchange with the hydrosphere and biosphere.
Dissolved mineral matter in soil is largely present as ions.
Prominent among the cations are H+, Ca2+, Mg2+, K+, Na+, and usually very low levels of Fe2+, Mn2+, and Al3+.
The last three cations may be present in partially hydrolized form, such as FeOH+, or complexed by organic humic substance ligands.
Anions that may be present are HCO3−, CO3 2−, HSO 4−, SO42−, Cl− and F −.
In addition to being bound to H+ in species such as bicarbonate, anions may be complexed with metal ions, such as in AlF2+.
Multivalent cations and anions form ion pairs with each other in soil solutions eg CaSO4 and FeSO4.

## Slide 18: Macronutrients in soil
Macronutrients are those elements that occur in substantial levels in plant materials or in fluids in the plant.
Essential macronutrients for plants are carbon, hydrogen, oxygen, nitrogen, phosphorus, potassium, calcium, magnesium, and sulfur.
Carbon, hydrogen, and oxygen are obtained from the atmosphere.
The other essential macronutrients must be obtained from soil are nitrogen, phosphorus and potassium and these are the most likely to be lacking and are commonly added to soil as fertilizers.

## Slide 19: Cont…
Calcium-deficient soils are relatively uncommon.
However, calcium uptake by plants and leaching by carbonic acid may produce a calcium deficiency in soil.
In alkaline soils, the presence of high levels of sodium, magnesium, and potassium sometimes produces calcium deficiency because these ions compete with calcium for availability to plants.
If calcium/magnesium ratio is too high, magnesium may not be available to plants and magnesium deficiency results.

## Slide 20: Cont…
Similarly, excessive levels of potassium or sodium may cause magnesium deficiency.
Soils deficient in sulfur do not support plant growth well, largely because sulfur is a component of some essential amino acids and of thiamin and biotin.
Nitrogen, phosphorus, and potassium are plant nutrients that are obtained from soil.
They are so important for crop productivity that they are commonly added to soil as fertilizers.

## Slide 21: Micronutrients in soil
Boron, chlorine, copper, iron, manganese, molybdenum (for N-fixation), and zinc are considered essential plant micronutrients.
These nutrients are toxic at higher levels.
Manganese, iron, chlorine, and zinc may be involved in photosynthesis.
Iron and manganese occur in a number of soil minerals.
Sodium and chlorine (as chloride) occur naturally in soil.
Other trace elements that occur as specific minerals, sulfide inclusions, or by isomorphic substitution for other elements in minerals includes chromium, cobalt, arsenic, selenium, nickel, lead, and cadmium.

## Slide 22: Cont…
The trace elements listed above may be coprecipitated with secondary minerals that are involved in soil formation.
Such secondary minerals include oxides of aluminum, iron, and manganese (precipitation of hydrated oxides of iron and manganese efficiently removes many trace metal ions from solution); calcium and magnesium carbonates; smectites; vermiculites; and illites.
Plants accumulating more than 1.00 mg/g of dry weight of specific trace metals are called hyperaccumulators.
Uranium accumulation in the plants was enhanced by the addition of citrate, which complexes uranium and makes it more soluble.

## Slide 23: 4.4. Reactions in soil
4.4.1. Acid-base and ion-exchange reactions in the soil
The more important chemical functions of soil is the exchange of cations in both the mineral and organic portions of soil.
Clay minerals exchange cations because of the presence of negatively charged sites on the mineral, resulting from the substitution of an atom of lower oxidation number for one of higher number, for example; magnesium for aluminum.
Organic materials exchange cations because of the presence of the carboxylate group and other basic functional groups.
Humus typically has a very high cation-exchange capacity.

## Slide 24: Cont…
Cation exchange in soil is the mechanism by which potassium, calcium, magnesium, and essential trace -level metals are made available to plants.
When nutrient metal ions are taken up by plant roots, H+ is exchanged for the metal ions.
This process, plus the leaching of calcium, magnesium, and other metal ions from the soil by water containing carbonic acid, tends to make the soil acidic:
Soil acts as a buffer and resists changes in pH.
The buffering capacity depends upon the type of soil.

## Slide 25: 4.4.2. Formation of Mineral Acid in Soil
The oxidation of pyrite in soil causes formation of acid-sulfate soils sometimes called ‘’cat clays”:
FeS2 + 7/2 O2 + H2O → Fe 2+ + 2H + + 2SO42−
Cat clay soils may have pH values << 3.0.
These soils are formed when neutral or basic marine sediments containing FeS2 become acidic upon oxidation of pyrite when exposed to air.
Appreciable levels of sulfate and a pH below 3.0 indicate potential to form acid-sulfate soils.

## Slide 26: Cont…
If the pH is above 3.0, either little FeS2 is present or sufficient CaCO3 is in the soil to neutralize the H2SO4 and acidic Fe3+.
Pyrite-containing mine spoils (residue from mining) also form soils similar to acid-sulfate soils of marine origin.
In addition to high acidity and toxic H2S, a major chemical species limiting plant growth on such soils.
Aluminum ion liberated in acidic soils is very toxic to plants.

## Slide 27: 4.4.3. Adjustment of Soil Acidity
Most common plants grow best in soil with a pH near neutrality.
If the soil becomes too acidic for optimum plant growth, it may be restored to productivity by liming, ordinarily through the addition of calcium carbonate:
In areas of low rainfall, soils may become too basic (alkaline) due to the presence of basic salts such as Na2CO3.
Alkaline soils may be treated with aluminum or iron sulfate, which release acid on hydrolysis:

## Slide 28: Cont…
Sulfur added to soils is oxidized by bacterially mediated reactions to sulfuric acid:
Sulfur is used, to acidify alkaline soils.
The huge quantities of sulfur now being removed from fossil fuels to prevent air pollution by sulfur dioxide may make the treatment of alkaline soils by sulfur much more attractive economically.

## Slide 29: 4.4.4. Ion Exchange Equilibria in Soil
Competition of different cations for cation exchange sites on soil cation exchangers can described semi-quantitatively by exchange constants.
Example, soil reclaimed from an flooded area with seawater will have most of its cation exchange sites occupied by Na+, and restoration of fertility requires binding of nutrient cations such as K+:
Where KC is the exchange constant which expresses the relative tendency of soil to retain K+ and Na+.
NK and NNa are the equivalent ionic fractions of potassium and sodium, bound to soil.

## Slide 30: Cont…
In many cases, the exchange of anions does not involve a simple ion-exchange process.
This is true of the strong retention of orthophosphate species by soil.
At the other end, nitrate ion is very weakly retained by the soil.
Anion exchange may be occurring at the surfaces of oxides in the mineral portion of soil.
At low pH, a metal oxide surface may have a net positive charge enabling it to hold anions, such as chloride, by electrostatic attraction as shown below where M represents a metal:

## Slide 31: Cont…
At higher pH values, the metal oxide surface has a net negative charge due to the formation of OH− ion on the surface caused by loss of H + from the water molecules bound to the surface:
In such cases, it is possible for anions such as HPO4 2− to displace hydroxide ion and bond directly to the oxide surface:

## Slide 32: 4.5. Wastes and Pollutants In Soil
Fertilizers has an effect to pollute soil.
Ammonia vapor is toxic and NH3 is reactive with some substances.
The alkali metal nitrates tend to make soil alkaline, whereas ammonium sulfate leaves an acidic residue.
Much of the sulfur dioxide emitted in the burning of sulfur-containing fuels ends up as soil sulfate.
Atmospheric nitrogen oxides are converted to nitrates in the atmosphere, and the nitrates eventually are deposited on soil.

## Slide 33: Cont…
Soil sorbs NO and NO2, and these gases are oxidized to nitrate in the soil.
Carbon monoxide is converted to CO2 and possibly to biomass by soil bacteria and fungi.
Particulate lead from automobile exhausts is found at elevated levels in soil along heavily traveled highways also it founds at elevated levels from lead mines and smelters .
Soil is the receptor of many hazardous wastes from landfill leachate, lagoons, and other sources.
polychlorinated biphenyls (PCBs) is the contaminant of soil.

## Slide 34: Cont…
Volatile organic compounds (VOC) in industrialized and areas such as benzene, toluene, xylenes, dichloromethane, trichloroethane, and trichloroethylene, may contaminate soil.
The degradation and eventual fate of pesticides on soil largely determines their ultimate environmental effects.
Adsorption by soil is a key aspect of pesticide degradation and plays a strong role in the speed and degree of degradation.
The degree of adsorption and the speed and extent of ultimate degradation are influenced by a number of other factors.

## Slide 35: Cont…
These includes solubility, volatility, charge, polarity and molecular structure and size, are properties of the medium.
Adsorption of a pesticide by soil components have several effects.
Chemical degradation reactions of pesticides may be catalyzed by adsorption.
The toxicity of an herbicide to plants may be reduced by sorption on soil.
The forces holding a pesticide to soil particles may be of several types.

## Slide 36: Cont…
Physical adsorption: involves dipole-dipole interactions between the pesticide molecule and charged soil particles.
Hydrogen bonding: in this mechanism also some pesticides are held to soil.
In some cases a pesticide may act as a Ligand coordinating to metals in soil mineral matter.
The three primary ways in which pesticides are degraded in / on soil are:
Chemical degradation : has been observed experimentally in soils and clays sterilized to remove all microbial activity.

## Slide 37: Cont…
2. photochemical reactions : is chemical reactions brought about by the absorption of light.
3. Biodegradation and the Rhizosphere: microorganisms have the most important role and insects, earthworms and plants degrade pesticides and other organic pollutants.
The rhizosphere is the layer of soil in which plant roots are especially active, is a particularly important part of soil with respect to biodegradation of wastes.
It increased biomass and is strongly influenced by the plant root system and the microorganisms associated with plant roots.

## Slide 38: Cont…
Among the organic species for which enhanced biodegradation in the rhizosphere are: (associated plant or crop shown in parentheses): 2,4-D herbicide (wheat, African clover, sugarcane, flax), parathion (rice, bush bean), carbofuran (rice), atrazine (corn), diazinon (wheat, corn, peas), volatile aromatic alkyl and aryl hydrocarbons and chlorocarbons (reeds), and surfactants (corn,soybean, cattails).
Enhanced biodegradation of polycyclic aromatic hydrocarbons (PAH) was observed in the rhizospheric zones of prairie grasses.

## Slide 39: CHAPTER -5
5. Environmental Toxicity and Toxicology
5. 1 Introduction
A poison, or toxicant, is a substance that is harmful to living organisms because of its detrimental effects on tissues, organs, or biological processes.
Toxicology is the science of poisons.
Whether a substance is poisonous depends upon the type of organism exposed, the amount of the substance, and the route of exposure.
In the case of human exposure, the degree of harm done by a poison can depend strongly upon whether the exposure is to the skin, by inhalation, or through ingestion.

## Slide 40: Cont…
Toxicants can be gases, vapours, dusts (respirable solids), fumes (solid particles from the condensation of vapors, often metals or metal oxides) and Mists (liquid droplets).
A substance with which the toxicant is associated is called matrix.
The matrix may have a strong effect upon the toxicity of the toxicant.
Variables related to the ways in which organisms are exposed to toxic substances includes dose and concentration of toxicants.
Dose is the amount, usually per unit body mass, of a toxicant to which an organism is exposed.

## Slide 41: Cont…
Response is the effect upon an organism resulting from exposure to a toxicant.
Both the duration of exposure (total time period) and the frequency of exposure (rate of exposure ) are both important situational variables.
The exposure site and route also affect toxicity.
Exposures can classify on the basis of acute vs. chronic and local vs. systemic exposure, giving four general categories.

## Slide 42: Cont…
Acute local exposure occurs at a specific location over a time period of a few seconds to a few hours and may affect the exposure site, particularly the skin, eyes, or mucous membranes.
The same parts of the body can be affected by chronic local exposure, for which the time span may be as long as several years.
Acute systemic exposure is a brief exposure or exposure to a single dose and occurs with toxicants that can enter the body, such as by inhalation or ingestion, and affect organs, such as the liver, those are remote from the entry site.
Chronic systemic exposure differs in that the exposure occurs over a prolonged time period.

## Slide 43: Cont…
The way that a toxic substance is introduced into an organism is depend on the physical and chemical properties of the substance.
The pulmonary system is most likely to take in toxic gases or very fine, respirable solid or liquid particles and solid can usually enters the body orally.
Absorption through the skin is most likely for liquids, solutes in solution, and semisolids, such as sludge.
Most exposures to animals are through ingestion or gavages (introduction into the stomach through a tube).

## Slide 44: Cont…
Example of the importance of the route of exposure to toxicants is provided by cancer is due to contact of coal tar with skin.
The major barrier to dermal absorption of toxicants is the stratum corneum , or horny layer.
When substances have the same physiologic function, their effects may be simply additive or they may be synergistic (the total effect is greater than the sum of the effects of each separately).
Potentiation occurs when an inactive substance enhances the action of an active one, and antagonism when an active substance decreases the effect of another active one.

## Slide 45: 5.2. Inorganic and Organic Pollutants
5.2.1. Toxic Inorganic Compounds
Cyanide: Both hydrogen cyanide (HCN) and cyanide salts are rapidly acting poisons; a dose of only 60–90 mg is kill a human.
Metabolically, cyanide bonds to Fe(III) in iron-containing ferricytochrome oxidase enzyme preventing its reduction to Fe(II) in the oxidative phosphorylation process by which the body utilizes O2.
This prevents utilization of oxygen in cells, so that metabolic processes cease.

## Slide 46: Cont…
Carbon monoxide (CO): When CO in air exposure is to 100 ppm causes dizziness, headache and tiredness; loss of consciousness occurs at 250 ppm; and inhalation 1,000 ppm results rapid death.
Chronic long-term exposures to low levels of CO are suspected of causing disorders of the respiratory system and the heart.
After entering the blood stream through the lungs, CO reacts with hemoglobin (Hb) to convert oxyhemoglobin (O2Hb) to carboxyhemoglobin (COHb):
O2Hb + CO → COHb + O2
Carboxyhemoglobin is much more stable than oxyhemoglobin so that its formation prevents hemoglobin from carrying oxygen to body tissues.

## Slide 47: Cont…
Nitrogen Oxides: The three oxides of nitrogen normally encountered in the atmosphere are nitrous oxide (N2O), nitric oxide (NO), and nitrogen dioxide (NO2).
Nitrogen dioxide (NO2): causes severe irritation of the innermost parts of the lungs resulting in pulmonary edema.
Fatalities may result from even brief periods of inhalation of air containing 200–700 ppm of NO2.
Biochemically, NO2 disrupts lactic dehydrogenase and some other enzyme systems, a stronger oxidant.
Free radicals, particularly HO·, are likely formed in the body by the action of NO2 and the compound probably causes lipid peroxidation in which the C=C double bonds in unsaturated body lipids are attacked by free radicals and undergo chain reactions in the presence of O2, resulting in their oxidative destruction.

## Slide 48: Cont…
Nitrous oxide, N2O (laughing gas): is used as an oxidant gas and in dental surgery as a general anesthetic.
Nitrous oxide is a central nervous system depressant and can act as an asphyxiant.
Nitric oxide (NO): is less toxic than NO2.
Like carbon monoxide and nitrite, NO attaches to hemoglobin and reduces oxygen transport efficiency.
However, in a polluted atmosphere, the concentration of nitric oxide normally is much lower than that of carbon monoxide so that the effect on hemoglobin is much less.

## Slide 49: Cont…
Hydrogen Halides: F and Cl are relatively toxic gases.
Fluoride ion (F¯), is toxic in soluble fluoride salts, such as NaF, causing fluorosis, a condition characterized by bone abnormalities and mottled, soft teeth.
However, about 1 ppm of fluoride used in some drinking water supplies prevents tooth decay.
Hydrogen fluoride, Causes extreme irritants to any part of the body that they contact and ulcers in affected areas of the upper respiratory tract.
Lesions caused by contact with HF heal poorly, tend to develop gangrene.

## Slide 50: Cont…
Gaseous & aqueous solution of HCl, are much less toxic than HF.
However, inhalation of HCl vapor can cause spasms of the larynx as well as pulmonary edema and even death at high levels.
The high affinity of hydrogen chloride vapor for water tends to dehydrate eye and respiratory tract tissue.
Inorganic Compounds of Silicon:
Silica (SiO2, quartz): occurs in a variety of types of rocks such as sand, sandstone, and diatomaceous earth.

## Slide 51: Cont…
A type of pulmonary fibrosis that causes lung nodules and makes victims more susceptible to pneumonia and other lung diseases, silicosis is one of the most common disabling conditions resulting from exposure.
It can cause death from insufficient oxygen, or from heart failure in severe cases.
Silicon tetrachloride and trichlorosilane, fuming liquids which react with water to give off HCl vapor, have suffocating odors and are irritants to eye, nasal and lung tissue.
Asbestos: The name given to a group of fibrous silicate minerals, typically those of the serpentine group, for which the approximate chemical formula is Mg3(Si2O5)(OH)4.

## Slide 52: Cont…
Inhalation of asbestos may cause asbestosis (a pneumonia condition) and bronchogenic carcinoma (cancer originating with the air passages in the lungs).
Inorganic Phosphorus Compounds : Phosphine (PH3), a colorless gas that undergoes autoignition at 100°C, is a potential hazard in industrial processes and in the laboratory.
Symptoms of potentially fatal phosphine gas include pulmonary tract irritation, depression of the central nervous system, fatigue, vomiting, and difficult painful breathing.

## Slide 53: Cont…
Because of the formation of acid and its dehydrating action, P4O10 is a corrosive irritant to skin, eyes and mucous membranes.
The phosphorus halides (PX3 and PX5) are strong irritants to eyes, skin, and mucous membranes.
The major phosphorus oxyhalide in commercial use is phosphorus oxychloride (POCl3), a faintly yellow fuming liquid.
Reacting with water to form toxic vapors of hydrochloric acid and phosphorous acid (H3PO3); phosphorus oxyhalide is a strong irritant to the eyes, skin, and mucous membranes.

## Slide 54: Cont…
Inorganic Compounds of Sulfur:
Hydrogen sulfide: A colorless gas with a foul, rotten-egg odor, and it is very toxic.
In some cases inhalation of H2S kills faster than hydrogen cyanide.
Rapid death ensues from air containing more than 1000 ppm H2S due to suffocation from respiratory system paralysis.
Lower doses cause symptoms include headache, dizziness and excitement due to damage the central nervous system.
General debility is one of the numerous effects of chronic H2S poisoning.
Sulfur dioxide, SO2: dissolves in water, to produce sulfurous acid, H2SO3; hydrogen sulfite ion, HSO3−; and sulfite ion, SO32−.
Because of its water solubility, it is largely removed in the upper respiratory tract.

## Slide 55: Cont…
It is an irritant to the eyes, skin, mucous membranes, and respiratory tract.
Some individuals are hypersensitive to sodium sulfite (Na2SO3), which has been used as a chemical food preservative.
sulfuric acid (H2SO4): is a severely corrosive poison and dehydrating agent in the concentrated liquid form
It readily penetrates skin to reach subcutaneous tissue causing tissue necrosis with effects resembling those of severe thermal burns.
Sulfuric acid fumes and mists irritate eye and respiratory tract tissue, and industrial exposure has even caused tooth erosion in workers.

## Slide 56: 5.2.2. Toxicology of Organic Compounds
Alkane Hydrocarbons: Gaseous methane, ethane, propane, n-butane, and isobutane (both C4H10) are regarded as simple asphyxiants that form mixtures with air containing insufficient oxygen to support respiration.
The most common toxicological occupational problem associated with the use of hydrocarbon liquids in the workplace is dermatitis, caused by dissolution of the fat portions of the skin and characterized by inflamed, dry, scaly skin.
Inhalation of volatile liquid 5–8 carbon n-alkanes and branched-chain alkanes may cause central nervous system depression manifested by dizziness and loss of coordination.

## Slide 57: Cont…
Exposure to n-hexane and cyclohexane results in loss of myelin (a fatty substance constituting a sheath around certain nerve fibers) and degeneration of axons (part of a nerve cell through which nerve impulses are transferred out of the cell).
This has resulted in multiple disorders of the nervous system (polyneuropathy) including muscle weakness and impaired sensory function of the hands and feet.
Alkene and Alkyne Hydrocarbons: Ethylene, a widely used colorless gas with a somewhat sweet odor, acts as a simple asphyxiant and anesthetic to animals and is phytotoxic (toxic to plants).

## Slide 58: Cont…
The toxicological properties of propylene (C3H6) are very similar to those of ethylene.
Colorless, odorless, gaseous 1,3 -butadiene is an irritant to eyes and respiratory system mucous membranes; at higher levels it can cause unconsciousness and even death.
Acetylene, C2H2, is a colorless gas with a garlic odor.
It acts as an asphyxiant and narcotic, causing headache, dizziness, and gastric disturbances.
Benzene and Aromatic Hydrocarbons: Inhaled benzene is readily absorbed by blood, from which it is strongly taken up by fatty tissues.

## Slide 59: Cont…
Benzene is a skin irritant, and progressively higher local exposures can cause skin redness (erythema), burning sensations, fluid accumulation (edema).
Inhalation of air containing about 7 g/m3 of benzene causes acute poisoning within an hour because of a narcotic effect upon the central nervous system manifested progressively by excitation, depression, respiratory system failure, and death.
Inhalation of air containing more than about 60 g/m3 of benzene can be fatal within a few minutes.

## Slide 60: Cont…
Long-term exposures to lower levels of benzene cause nonspecific symptoms, including fatigue, headache, and appetite loss.
Chronic benzene poisoning causes blood abnormalities, including a lowered white cell count, an abnormal increase in blood lymphocytes (colorless corpuscles introduced to the blood from the lymph glands), anemia, a decrease in the number of blood platelets required for clotting, damage to bone marrow and cancer.
Oxygen-Containing Organic Compounds:
Alcohols: Methanol products affect the central nervous system and the optic nerve.

## Slide 61: Cont…
Acute exposure to lethal doses causes an initially mild inebriation, followed by unconsciousness, cardiac depression and death.
Sub-lethal exposures can cause blindness from deterioration of the optic nerve and retinal ganglion cells.
Inhalation of methanol fumes may result in chronic, low-level exposure.
Ethanol has numerous acute effects resulting from central nervous system depression.
These range from decreased inhibitions and slowed reaction times at 0.05% blood ethanol, through intoxication, stupor, and at more than 0.5% blood ethanol death.
Ethanol also has a number of chronic effects, of which the addictive condition of alcoholism and cirrhosis of the liver are the most prominent.

## Slide 62: Cont…
Inhaling of ethylene glycol initially stimulates the central nervous system and then depresses it.
Glycolic acid (HOCH2CO2H) formed as an intermediate metabolite in the metabolism of ethylene glycol, may cause acidemia, and oxalic acid produced by further oxidation may precipitate in the kidneys as solid calcium oxalate, CaC2O4, causing clogging.
Of the higher alcohols, 1-butanol is an irritant, but its toxicity is limited by its low vapor pressure.
Unsaturated (alkenyl) allyl alcohol, CH=CHCH2OH, has a pungent odor and is strongly irritating to eyes, mouth and lungs.

## Slide 63: Cont…
Phenols: The acute toxicological effects of phenol are largely upon the central nervous system and death can occur as soon as after exposure.
Acute poisoning by phenol can cause severe gastrointestinal disturbances, kidney malfunction, circulatory system failure, lung edema and convulsions.
Fatal doses of phenol may be absorbed through the skin.
Key organs damaged by chronic phenol exposure include the pancreas and kidneys.

## Slide 64: Cont…
Aldehydes and Ketones: Exposure to inhaled formaldehyde via the respiratory tract is usually due to molecular formaldehyde vapor, whereas exposure by other routes is usually due to formalin.
Prolonged, continuous exposure to formaldehyde can cause hypersensitivity.
Formaldehyde has been shown to be a lung carcinogen.
The toxicity of formaldehyde is largely due to its metabolic oxidation product formic acid.

## Slide 65: Cont…
However, aldehydes that are relatively less soluble can penetrate further into the respiratory tract and affect the lungs.
Colorless, liquid acetaldehyde is relatively less toxic than acrolein and acts as an irritant and systemically as a narcotic to the central nervous system.
Pleasant-smelling acetone can act as a narcotic; it causes dermatitis by dissolving fats from skin.
Not many toxic effects have been attributed to methyl ethyl ketone.
It is suspected of having caused neuropathic disorders in shoe factory workers.

## Slide 66: Cont…
Organonitrogen Compounds:
Aliphatic Amines: The lower amines, such as the methylamines, are rapidly and easily taken into the body by all common exposure routes.
They are basic and react with water in tissue:
R3N + H2O → R3NH+ + OH−
  raising the pH of the tissue to harmful levels, acting as corrosive poisons (especially to sensitive eye tissue), and causing tissue distruction at the point of contact.
Among the systemic effects of amines are necrosis (destruction) of the liver and kidneys, lung hemorrhage (bleeding)and edema and sensitization of the immune system.

## Slide 67: Cont…
The lower amines are among the more toxic substances in routine, large-scale use.
Alkyl polyamines have toxicity rating only 3, but it is a strong skin sensitizer and can damage eye tissue.
Carbocyclic Aromatic Amines: is a widely used industrial chemical and.
Some of the carbocyclic aromatic amines have been shown to cause cancer in the human bladder, ureter, and pelvis and are suspected of being lung, liver and prostate carcinogens.
Aniline is the simplest of the carbocyclic aromatic amines and it is a very toxic colorless liquid and distinct odor.

## Slide 68: Cont…
Aniline readily enters the body by inhalation, ingestion and through the skin.
Metabolically, aniline converts iron(II) in hemoglobin to iron(III).
This causes a condition called methemoglobinemia, characterized by cyanosis and a brown-black color of the blood, in which the hemoglobin can no longer transport oxygen in the body.
Pyridine: a colorless liquid with a sharp, penetrating, terrible odor.
Symptoms of pyridine poisoning include anorexia, nausea, fatigue and in cases of chronic poisoning, mental depression.
In a few rare cases pyridine poisoning has been fatal.

## Slide 69: Cont…
Nitriles: contain the -CN functional group.
Colorless, liquid acetonitrile, CH3CN, is widely used in the chemical industry.
It has caused human deaths, perhaps by metabolic release of cyanide.
Acrylonitrile: ingested, absorbed through the skin, or inhaled as vapor, acrylonitrile metabolizes to release deadly HCN, which it resembles toxicologically.

## Slide 70: Cont…
Nitro Compounds: The simplest of the nitro compounds, nitromethane H3CNO2, is an oily liquid that causes anorexia, diarrhea, nausea, and vomiting, and damages the kidneys and liver.
Nitrobenzene, a pale yellow, oily liquid with an odor of bitter almonds or shoe polish, can enter the body by all routes.
It has a toxic action much like that of aniline, converting hemoglobin to methemoglobin, which cannot carry oxygen to body tissue.
Nitrobenzene poisoning is manifested by cyanosis.

## Slide 71: Cont…
Organosulfur compounds: Inhalation of even very low concentrations of the alkyl thiols, such as methanethiol, H3CSH, can cause nausea and headaches; higher levels can cause increased pulse rate, cold hands and feet, and cyanosis.
In extreme cases, unconsciousness, coma and death occur.
An oily, water-soluble liquid, methylsulfuric acid is a strong irritant to skin, eyes, and mucous tissue.
Colorless, odorless dimethyl sulfate is highly toxic and is a primary carcinogen that does not require bioactivation to cause cancer.

## Slide 72: Cont…
Damage to the liver and kidneys, pulmonary edema, cloudiness of the cornea, and death within 3–4 days can result from heavier exposures.
Sulfur Mustards: A typical example of deadly sulfur mustards, compounds used as military poisons, or ‘’poison gases”, is mustard oil (bis(2-chloroethyl)sulfide).
This military ‘’blistering gas” poison causes tissue to become severely inflamed with lesions that often become infected.
These lesions in the lung can cause death.

## Slide 73: Cont…
Organophosphorus Compounds: These compounds have varying degrees of toxicity.
Organophosphorus Military Poisons: A systemic poison to the central nervous system that is readily absorbed as a liquid through the skin, Sarin may be lethal at doses as low as about 0.0l mg/kg; a single drop can kill a human.
Organophosphate Esters: Trimethyl phosphate is moderately toxic when ingested or absorbed through the skin, whereas moderately toxic triethyl phosphate, (C2H5O)3PO, damages nerves and inhibits acetylcholinesterase.

## Slide 74: 5.3. Agricultural and pharmaceutical contaminants
5.3.1. Agricultural contaminants
There are a number of common agricultural activities that are significant sources of pollution.
The most common chemical contaminants in drinking-water sources arising from agricultural activity are nitrate and pesticides.
Human excrement (night soil), animal manures, fertilizers and biosolids (sewage sludge) used for agricultural purposes may be a source of excess nutrients, particularly phosphorus, which can contribute to algal blooms in slow flowing or still bodies of water.

## Slide 75: Cont…
Health risks from water contamination include acute poisoning, irritations, cancers, brain tumors, birth defects, infertility, other disruptions of the endocrine system, cognitive impairment, and other neurodevelopmental effects that can stem from chronic exposure.
Toxic algae and less visible contaminants, ranging from nitrates (especially in groundwater) and ammonia, to pesticides, fecal pathogens, heavy metals, and plastic leachates, can leave households with water that is unsafe for drinking or other uses.
In drinking water, for example, high concentrations of nitrates left behind by animal feces and fertilizer are thought to cause methemoglobinemia (blue baby syndrome), with chronic exposure to lower doses potentially increasing the risk of cancer and other health problems.

## Slide 76: Cont…
Agricultural pollution, in both its acute and chronic forms, is a major threat to crop and animal biodiversity, and species losses can be irreversible even after pollution ceases.
Rates of terrestrial nitrogen deposition have been associated with biodiversity losses.
Nitrogenous fertilizer are the primary emitter of nitrous oxide (N2O) and methane (CH4), as well as a source of other long-lived and short-lived climate pollutants, agriculture is contributing significantly to both long-term and short-term climate warming.
Synthetic fertilizer use is the leading source of agricultural greenhouse gases

## Slide 77: Cont…
Fine particle and other emissions from agricultural burning, improper manure storage, and fertilizer and pesticide use contribute to air pollution like smog formation, air pollution and related disease.
Soil acidification can be accelerated by farming practices such as irrigation, fertilization, and the removal of crop residues from farmland.
Ground-level ozone, the formation of which is enhanced by nitrogenous emissions (including from fertilizer and manure management), is known to have a damaging effect on crops and vegetation.

## Slide 78: 5.3.2. pharmaceutical contaminants
People can be exposed to pharmaceutical residues in their diet in a number of ways, including via crops (from uptake due to the use of contaminated manure and sewage sludge), fishery products, meat and dairy products, as well as from drinking contaminated tap water.
Antibiotics, anti-parasitics, antimycotics (anti-fungals) and anticancer medicines are groups of chemicals intended to kill their target organism or target cells.
Pharmaceuticals enter the environment through Human and animal excretion.

## Slide 79: Cont…
A large portion of the pharmaceuticals in our water come from the improper disposal of unused or unwanted drugs by households and medical facilities.
Their most popular uses are include human medicine veterinary drugs or husbandry growth promoters with applications on many different aspects of agriculture.
pharmaceuticals can be found everywhere, including sediment, medical sewage, surface water, groundwater, drinking water, in the arctic environment and in biota.

## Slide 80
Fig.. Routes of both veterinary and human pharmaceutical substances in the environment

## Slide 81: 5.4. Pesticides
A pest, broadly defined, is any organism plant, animal, or microorganism that is destructive or trouble some or living where it is unwanted.
Pesticides refer to any chemicals intended to prevent, destroy, or otherwise impair the ability of pests to compete with desired organisms, such as crops, animals or humans.
Pesticides can be classified in different ways, such as by their target, chemical nature, physical state and mode of action.
Classification based on the target is perhaps the most widely known: insecticides, herbicides, fungicides and rodenticides.

## Slide 82: 5.4.1. Insecticides
Insecticides are those compounds that are effective against insects.
While most insecticides are applied as sprays, others are applied as dusts, aerosols, fumigants and baits.
The majority of insecticides used today are synthetic organic chemicals, and most of them are nerve poisons.
Exhibiting a wide range of kind and degree of toxic effects, many organohalide insecticides affect the central nervous system, causing tremor, irregular eye jerking, changes in personality, and loss of memory.
Such symptoms are characteristic of acute DDT poisoning.

## Slide 83: Cont…
However, the acute toxicity of DDT (2,2-bis [p-chlorophenyl]-1,1,1-trichloroethane or dichloro-diphenyl trichloroethane) to humans is very low and, when used for the control of typhus and malaria.
The chlorinated cyclodiene insecticides— aldrin, dieldrin, endrin, chlordane, heptachlor, endosulfan, and isodrin—act on the brain, releasing betaine esters causing headaches, dizziness, nausea, vomiting, jerking muscles, and convulsions.

## Slide 84: Cont…
Dieldrin, chlordane and heptachlor have caused liver cancer in, and some chlorinated cyclodiene insecticides are teratogenic or fetotoxic and because of their effects aldrin, dieldrin, heptachlor, and more recently chlordane they have been prohibited from use .
Typically, DDT and other chlorinated hydrocarbons are persistent broadspectrum insecticides.
Their residues persist in the environment for long periods.
DDT

## Slide 85: Cont…
Organophosphorus insecticides are the most toxic among the insecticides; they are dangerous not only to insects but also to mammals.
Many of these compounds, such as parathion, paraoxon, timet, and tetram are in the ‘‘super toxic’’ category of human poisons.
Human fatal doses for these toxicants are <5 mg/kg, along with arsenic (As), cyanide (CN−) and some others.
As little as 2 mg of parathion has been known to kill children.
Other organophosphorus insecticides are parathion, malathion, and tetraethyl pyrophosphate (TEPP).

## Slide 86: Cont…
Organophosphate insecticides Symptoms of poisoning in humans include nausea, vomiting, diarrhea, cramps, sweating, salivation, blurred vision, fatal due to respiratory failure and muscular tremors.
Even though organophosphates are usually more toxic to humans and mammals than chlorinated hydrocarbons, they are more easily biodegraded than the organochlorines.

## Slide 87: Cont…
Carbamates: are derivatives of carbamic acid (HO–CO–NH2). Carbamates are widely used for worm control on vegetables.
Carbamates include aldicarb (2-methyl-2 [methylthio]propionaldehyde-O-[methylcarbamoyl] oxime).
The contaminated melons had concentrations up to 3 ppm.
Symptoms resembled those of influenza, i.e., blurred vision, perspiration, nausea, dizziness, and shaking.
These symptoms usually not fatal and disappear after a few hours.

## Slide 88: 5.4.2. HERBICIDES
The most commonly used herbicides are phenoxyherbicides (PHs) that are 2,4-D (2,4-dichlorophenoxy acetic acid) and 2,4,5-T (2,4,5-trichlorophenoxy acetic acid).
After application, the chemicals are absorbed primarily through stomata and secondarily through root hairs with water.
In sensitive plants, the chemicals disrupt growth and various metabolic processes as they are translocated through vascular tissue.
Growth and metabolic processes are affected by the stimulation or inhibition of many enzymes, possibly leading to plant death.

## Slide 89: Cont…
Clinical symptoms of severely poisoned farmers include pain and weakness in the lower extremities, slowed nerve conduction velocity, twitching, and muscle spasms.
In addition, behavioral changes, such as nervousness, inability to concentrate, irritability, impotence and others may occur.

## Slide 90: 5.5. PCB’s(polychlorinated biphenyls)
Polychlorinated biphenyls (PCBs) are a class of synthetic chlorinated organic compounds with biphenyl as the basic structural unit.
Because of their wide use and resistance to degradation in the environment, PCBs are known as one of the major organochlorine pollutants found in the environment.
The chemical structure of PCB is
Where numbers are the possible sites for Cl atom.

## Slide 91: Cont…
Extensive PCB-contamination exists in the food chain.
The properties of PCBs are similar to those of DDT.
PCBs are soluble in fat or fat-solvents, but are hardly soluble in water.
Their solubility in water generally decreases with increase in the degree of chlorination.
They are non-drying and non-flammable, they are not affected by boiling with NaOH solutions.
Electrically, nonconducting, have very low vapor pressures.
PCB tend to bind tightly to particulate matter, such as soils and sediments.

## Slide 92: Cont…
Industrial uses include manufacture of plastics, paints, varnishes, asphalt, rubber, carbon paper, carbonless paper, printing inks, synthetic adhesives, sealers in waterproof material, lubricating oils, fire retardants, electrical transformers, and capacitors in the power industry.
The toxicity of technical PCB mixtures may be due to the presence of trace levels of several PCB congeners with four or more Cl atoms at both para and meta positions in the biphenyl rings but no Cl atoms.

## Slide 93: Cont…
possible coplanar PCB congeners 3,3’, 4, 4’-tetrachlorobiphenyl, 3,3’, 4,4’, 5-pentachlorobiphenyl and 3,3’,4,4’, 5,5’-hexachlorobipheynyl were found to be the most toxic.
These three coplanar congeners and dioxin were considered responsible for eliciting toxic effects in laboratory animals, including body weight loss, dermal disorder, hepatic damage, thymic atrophy, teratogenicity, reproductive toxicity, and immuno toxicity.

## Slide 94: Cont…
The symptoms included increased whitish eye discharge and swelling of the upper eyelids, pigmentation of nails, skin and mucous membranes, acne-like skin eruption (chloracne) with secondary infections, feelings of weakness, headache, and vomiting.
Three to four years after both incidences, the skin of those people who were only mildly poisoned appeared normal, yet systematic disorders, including dullness, cough, headache, stomachache, and swelling and pain of the joints, persisted.

## Slide 95: 5.6. Toxic heavy metals and organometallic compounds
5.6.1. Organometallic compounds
Organometallic compounds have an organic nature and higher lipid solubility.
Organolead Compounds: Perhaps the most notable toxic organometallic compound is tetraethyllead, Pb(C2H5)4, a colorless, oily liquid that was widely used as a gasoline additive to boost octane rating.
Tetraethyllead has a strong affinity for lipids and can enter the body by all three common routes of inhalation, ingestion, and absorption through the skin.
It affects the central nervous system with symptoms such as fatigue, weakness, restlessness, ataxia, psychosis, and convulsions.

## Slide 96: Cont…
Recovery from severe lead poisoning tends to be slow.
In cases of fatal tetraethyllead poisoning, death has occurred as soon as one or two days after exposure.
Organotin Compounds: Those of tin tributyltin chloride and related tributyltin (TBT) compounds are the greatest number of organometallic compounds in commercial use.
These compounds have bactericidal, fungicidal, and insecticidal properties.
Organotin compounds are readily absorbed through the skin, sometimes causing a skin rash.
They probably bind with sulfur groups on proteins and appear to interfere with mitochondrial function.

## Slide 97: 5.6.2. Toxic heavy metals
Heavy metals are toxic in their chemically combined forms and some, notably mercury, are toxic in the elemental form.
Mercury: Although several forms of ore occur, the principal one is cinnabar, the red sulfide, HgS.
Elemental mercury vapor can enter the body through inhalation and be carried by the bloodstream to the brain where it penetrates the blood-brain barrier.
It disrupts metabolic processes in the brain causing tremor and psychopathological symptoms such as shyness, insomnia, depression, and irritability.

## Slide 98: Cont…
Divalent ionic mercury, Hg2+, damages the kidney.
Organometallic mercury compounds such as dimethylmercury, Hg(CH3)2, are also very toxic.
2. Lead: It occurs naturally, in small amounts, in the air, surface waters, soil and rocks.
widely distributed as metallic lead, inorganic compounds, and organometallic compounds, has a number of toxic effects, including inhibition of the synthesis of hemoglobin.
It also adversely affects the central and peripheral nervous systems and the kidneys.
Pb poisoning may cause anemia.

## Slide 99: Cont…
It affects on the gastrointestinal tract include nausea, anorexia, and severe abdominal cramps (lead colic) associated with constipation.
Pb poisoning is also manifested by muscle aches and joint pain, lung damage, difficulty in breathing, and diseases such as asthma, bronchitis, and pneumonia.
Pb poisoning can also damage the immune system, interfering with cell maturation and skeletal growth.
Pb can pass the placental barrier and may reach the fetus, causing miscarriage, abortions and stillbirths.

## Slide 100: Cont…
3. Arsenic: is a metalloid which forms a number of toxic compounds.
The toxic +3 oxide, As2O3, is absorbed through the lungs and intestines.
Biochemically, arsenic acts to coagulate proteins, forms complexes with coenzymes, and inhibit the production of adenosine triphosphate (ATP) in essential metabolic processes involving the utilization of energy.
The result of its ingestion is through well water.
It has a symptoms of arsenicosis, manifested by skin discoloration and other symptoms.
Trivalent arsenic is much more toxic than pentavalent arsenic.

## Slide 101: Cont…
Arsenate is well absorbed and rapidly eliminated, mainly in urine.
Arsenite is also well absorbed, but is retained in greater quantities and for longer periods in tissues.
4. Chromium: It has different ores and it also exists in several oxidation states, but the most stable and common forms are Cr (0), the trivalent Cr (III), and the hexavalent Cr (VI) species.
Cr(VI) in the forms of chromate (CrO42−), dichromate (Cr2O42−), and CrO3 is considered the most toxic forms of chromium, as it presents high oxidizing potential, high solubility, and mobility across the membranes in living organisms and in the environment.

## Slide 102: Cont…
Cr (III) in the forms of oxides, hydroxides, and sulphates is less toxic as it is relatively insoluble in water, presents lower mobility, and is mainly bound to organic matter in soil and aquatic environments.
Chromium(III) compounds and chromium metal are not considered a health hazard, while chromium(VI) has the toxicity and carcinogenic properties.

## Slide 103: CHAPTER 6
6.1. INTRODUCTION
Green chemistry: is a sustainable, safe and non-polluting practice of chemical science and manufacturing, that consumes minimum amount of materials and energy while producing little or no waste product.
There are twelve green chemistry principles:
Prevention: Try not to make waste,

## Slide 104: Cont…
2. Atom economy: The final product should aim to contain all the atoms used in the process.
3. Less hazardous chemical synthesis: Wherever it is possible, production methods should be designed to make substances that are less toxic to people or the environment.
4. Designing safer chemicals: Chemical products should be designed to do minimum harm to people or the environment.
5. Safer solvents: When making materials try not to use solvents or other unnecessary chemicals.
If they are needed then they should not be harmful to the environment in any way.

## Slide 105: Cont…
6. Design for energy efficiency: The energy needed to carry out a reaction should be minimized to reduce environmental and economic impact. If possible carried out at ambient temperatures and pressures.
7. Use of renewable feed stocks: A raw material should be renewable wherever possible.
8. Reduce derivatives: Try not to have too many steps in the reaction because this means more reagents are needed and more waste is made.
9. Catalysis: Reactions that are catalysed are more efficient than uncatalysed reactions.

## Slide 106: Cont…
10. Design for degradation: When chemical products are finished with, they should break down into substances that are not toxic and do not stay in the environment.
11. Real-time analysis for pollution prevention: Methods need to be developed so that harmful products are detected before they are made.
12. Inherently safer chemistry for accident prevention: Substances used in a chemical process should be chosen to minimise the risk of chemical accidents, including explosions and fire.

## Slide 107: 6.2. The concept of atom economy
Atom economy refers to the ratio of molecular mass of desired product to the total molecular masses of materials generated.
The concept of atom economy can be illustrated in general by the reaction:
(Reactant)1 + (reactant)2 +…+ (reactant)n →product + by-product
The ultimate in atom economy is achieved when there is no by-product, and all the reagents are contained within the product.
Although this is often not practically possible, it is desirable to device reaction schemes such that by-product << product.

## Slide 108: 6.2.1. Some inherently atom economic reactions
By their very nature some reaction types are likely to produce less waste than others by virtue of being inherently atom efficient.
The factors taken into account in determining the most efficient, competitive and eco-friendly route are:
  Cost and availability of raw materials
  Devising a synthetic strategy.
  Toxicity/hazardous nature of raw materials
  Yield
  Ease of product isolation and purification
  Solvent requirements
  Energy requirements
  Equipment requirements, cost and availability
  Process times
  Nature of waste materials

## Slide 109: 6.2.2. Some inherently atom uneconomic reactions
These reactions should be viewed with caution when designing green syntheses and, if a viable alternative is not possible, attempts made either to recycle or to find a use for the eliminated or substituted product.
The Wittig reaction is useful for forming carbon–carbon double bonds and is widely used industrially in the manufacture of vitamins and pharmaceuticals.
It is an inherently wasteful reaction producing a mole equivalent of phosphine oxide per mole of product.
The phosphine oxide normally is converted to calcium phosphate for disposal.
It is this 0% phosphorus atom efficiency makes the Wittig reaction expensive, as well as environmentally problematic, and limits its usefulness.

## Slide 110: 6.3. Design and Application of Surfactants for Carbon Dioxide;
Surfactants
Surfactants are molecules that contain a polar portion and a non-polar portion.
A surfactant can interact with polar and non- polar molecules.
A surfactant increases the solubility of the otherwise insoluble substances.
In water, surfactant molecules tend to cluster into a spherical geometry non polar ends on the inside of the sphere polar ends on the outside these clusters are called micelles.

## Slide 111: Cont…
A Surfactant for Liquid or Supercritical Fluid CO2
Surfactants have both CO2-philic (CO2 loving) and CO2–phobic functionality.
Because of its low cost, wide availability, and environmentally and chemically benign nature, CO2 is an attractive solvent alternative for a wide variety of chemical and industrial processes.
The design and characterization of surfactants that enhance the solubilizing properties of CO2 is therefore crucial for its widespread application.
Substances that are normally considered to be gases take on special properties when highly compressed.

## Slide 112: Cont…
The most widely studied supercritical fluid is that formed by CO2 for which Tc = 31.1 oc and Pc = 73.8atm.
An important characteristic of supercritical fluids is their much lower viscosities than the conventional liquids; that of supercritical CO2 is only about 1/30 the viscosity of liquids normally used as solvents.
This allows solutes to diffuse much more readily in supercritical fluids, thus enabling them to react much faster.

## Slide 113: Cont…
A major advantage of supercritical fluid CO2 in some applications is that it is readily evaporated from solutes by releasing pressure.
With the appropriate apparatus, the released CO2 can be re-compressed back to a supercritical state for recycling.
A further advantage of supercritical fluid CO2 as a solvent is its ability to dissolve gases enhanced by the very high pressure.
Several laboratories have demonstrated progress in the micellization of aqueous and polar materials in many dense Supercritical fluids including alkanes, chlorofluorocarbons, hydrofluorocarbons, and CO2.

## Slide 114: Cont…
Supercritical CO2 (scCO2) fluid having reversed micelles with encapsulated aqueous cores, in other words, water-in-scCO2 (W/scCO2) microemulsion, is expected to behave as a universal solvent, since such an organized fluid has an attractive characteristics of scCO2 as well as a solvating properties of bulk water.
A promising lead for the design of highly effective surfactants for CO2 arose out of two related discoveries:
    CO2 is thermodynamically a good solvent for fluorinated acrylate polymers and
    These same polymers could be synthesized under homogeneous conditions in CO2.

## Slide 115: Cont…
Solubility of Substances in CO2
Carbon dioxide a nonpolar molecule since the dipoles of the two bonds cancels one another.
Carbon dioxide will dissolve smaller non polar molecules hydrocarbons having less than 20 carbon atoms other organic molecules such as aldehydes, esters, and ketones.
But it will not dissolve larger molecules such as oils, waxes, grease, polymers, and proteins, or polar molecules.

## Slide 116: 6.4. Designing an environmentally safe marine synthetic antifoulant
The settlement and accumulation of marine organisms (bio-fouling) on an inanimate substrate can cause large penalties to engineered structures.
In heat exchangers, biofouling can clog systems and on ship hulls it can increase the hydrodynamic drag, lower the maneuverability of the vessel and increase the fuel consumption.
This leads to increased costs within the shipping industry through the increased use of manpower, fuel, material and dry docking time.
It is agreed that there is a sequence of events to biofouling and the first stage is usually taken to be the formation of a biofilm.

## Slide 117: Cont…
Engineered structures such as ships and marine platforms, as well as offshore rigs and jetties, are under constant attack from the marine environment.
These structures need to be protected from the influences of the key elements of the marine environment such as saltwater, biological attack and temperature fluctuations.
Many traditional antifouling systems are paints.
Antifoulants are one of many additives usually incorporated within the topcoat paint of a marine protective coating system.
Most antifouling coatings are organic and consist of a primer and a topcoat both of which can include anticorrosive functions, however, the topcoat is often porous